## Slide 1: FastWake: Revisiting Host Network Stack for Interrupt-mode RDMA
Bojie Li1 Zihao Xiang1 Xiaoliang Wang2 Han Ruan1 Jingbin Zhou1 Kun Tan1
1Huawei 2Nanjing University
Presenter: Bojie Li, Computer Network and Protocol Lab, Huawei

## Slide 2: Interrupt-mode RDMA wastes the low latency of NICs

## Slide 3: Emergence of Microsecond Events
LUIZ BARROSO, MIKE MARTY, DAVID PATTERSON, AND PARTHASARATHY RANGANATHAN, Attack of the Killer Microseconds, Communications of the ACM, 2017.

## Slide 4: Why microsecond-scale latencies are hard to hide
CPU Instruction Pipeline
OS Process Scheduling
Nanosecond-scale latencies can be hidden by CPU out-of-order execution pipeline.
Example: DRAM access takes 50~100 ns, where the CPU core can execute independent instructions after the DRAM access.
CPU out-of-order pipeline only supports hundreds of instructions, so microsecond-scale latencies would stall the pipeline and decrease the efficiency of CPU.
OS process scheduling is designed to hide millisecond-scale latencies.
Context switching to another process takes 3~5us.
RDMA Read takes only 2~3us.
If we context switch to another process after sending the RDMA Read request, and switch back after receiving the RDMA response, then the CPU is wasted on process scheduling.
Task 1
a = *p; // memory access
b = c + d;
e = b + c;
d = b + d;
c = b + c;
f = b + a; // stall for memory access
Out-of-order execution
Traditional TCP
TCP send
Task 2
Task 3
TCP recv
context switch
context switch
Task 1
RDMA Read
Task 2
Task 3
RDMA Read response
context switch
context switch
RDMA

## Slide 5: Why interrupt-mode RDMA has high latency?
RDMA NIC
App Thread
CQ1
Kernel
EQ
interrupt
Interrupt handler
Context switch
①
②
③
④
⑨
Tasklet
Scheduler
⑤
⑧
Inter-Processor Interrupt
⑥
⑦
CQ: Completion Queue.
  Each CQ has a completion vector, which determines the CPU cores to deliver interrupts
EQ: Event Queue for interrupt notification.
  A completion vector corresponds to an EQ in kernel-mode host memory.
  EQ entries contain CQ numbers to notify.
①②③ NIC: 1.5 us
④⑤⑦ kernel (same core): 2.2 us
④⑤⑥⑦ kernel (different cores): 6.9 us
⑧ context switch: 0.3 us

## Slide 6: Key Observation 1
Direct context switch is much faster than process scheduling.
  Mutex and semaphore are IPC primitives provided by the kernel that achieves context switch by process scheduling.
Chart: 
| Context switch | Semaphore IPC (same core) | Pipe IPC (same core) | Semaphore IPC (other core) | Pipe IPC (other core)
系列 1 | 0.32 | 3.29 | 3.96 | 7.39 | 7.82
while (true) {
sched_yield();
}
while (true) {
sched_yield();
}
Thread 1
Thread 2
Kernel (context switch)
Context switch
Mutex/Semaphore
while (true) {
lock(&g_mutex);
unlock(&g_mutex);
}
Thread 1
Thread 2
Kernel (thread scheduling)
while (true) {
lock(&g_mutex);
unlock(&g_mutex);
}

## Slide 7: Approach 1: per-core dispatcher thread
RDMA NIC
App Thread 1
App Thread 2
Dispatcher Thread
CQ1
CQ2
Kernel context switch
Peek CQE
Peek CQE
①
②
③
④
The CQ is mapped to both application thread and a per-core dispatcher thread.
NIC sends CQE to the CQ.
Dispatcher thread polls all CQs on the core and peeks CQE from the CQ, but do not pop it out of CQ.
Dispatcher thread context switches to the application thread directly.
The application thread pops the CQE out of CQ.
When the application waits on the next event, it context switches back to the dispatcher thread.
⑤

## Slide 8: How to implement direct context switch?
Linux does not support context switching to a specific thread.
We introduce a new system call switch_to(pid)
  Simply checks the permission and puts the thread pid to the head of runqueue.
  Performance: 0.3~0.4 us.
Security:
  To avoid switch_to(pid) being abused to starve other threads, we only allow non-dispatcher threads to switch to dispatcher threads and only allow dispatcher threads to switch to non-dispatcher threads.
    We introduce a flag bit in the process control block to indicate whether it is a dispatcher thread.
Limitations:
  Direct context switch makes application threads have high priority than other threads with the same priority. However, because each priority has its own runqueue, threads with higher priority still takes precedence.

## Slide 9: Key Observation 2
Interrupt delivery to a thread running on the same core is much faster than other cores.
Reason: inter-processor interrupts (IPI) to wake up another core.

## Slide 10: Approach 2: interrupt core affinity & shorten kernel path
How to make sure interrupts and the thread are on the same core?
CQ1
CQ3
Thread 1
Thread 3
EQ1
create_cq(..., comp_vector=1)
create_cq(..., comp_vector=2)
Thread 2
CQ2
Core 1
Core 2
create_cq(..., comp_vector=1)
CQ4
Thread 4
create_cq(..., comp_vector=2)
EQ2
RDMA
NIC
EQEs including CQ numbers
EQEs including CQ numbers
MSIX interrupt
Completion vectors
Core 1
ISR
Core 2
ISR
Wake up threads
Wake up threads

## Slide 11: Approach 2: interrupt core affinity & shorten kernel path
What if the creator of the CQ and the user of the CQ are in different threads and on different cores?
What if a thread migrates to another core?
We need to dynamically update the affinity between CQs and EQs.
We leverage a feature in Mellanox NICs: CQ-to-EQ remapping.
The remapping is done lazily when the interrupt handler finds the thread to wake up is not on the same core.

## Slide 12: Approach 2: interrupt core affinity & shorten kernel path
CQ1
CQ1
Thread 1
Thread 1’
EQ1
create_cq(..., comp_vector=1)
modify_cq(..., comp_vector=2)
Core 1
Core 2
EQ2
RDMA
NIC
EQEs including CQ numbers
EQEs including CQ numbers
MSIX interrupt
Completion vectors
Core 1
ISR
Core 2
ISR
Inter-processor interrupt (IPI)
Wake up thread
Do CQ-to-EQ remapping when interrupt and thread are on different cores.
Thread migration

## Slide 13: Approach 2: interrupt core affinity & shorten kernel path
RDMA NIC
App Thread
CQ1
Kernel
EQ
interrupt
Interrupt handler
Context switch
①
②
③
④
⑤
⑥
RDMA NIC
App Thread
CQ1
Kernel
EQ
interrupt
Interrupt handler
Context switch
①
②
③
④
⑨
Tasklet
Scheduler
⑤
⑧
Inter-Processor Interrupt
⑥
⑦
Compared to traditional interrupt delivery path:
Remove tasklet and handle interrupts in top half.
  Top-half cannot use locks and dynamically allocated memory that may lead to sleep, so we remove them.
Directly put the thread to wake up at the head of the runqueue, bypassing the kernel scheduler.
Other minor optimizations (see the paper).

## Slide 14: FastWake system architecture
RDMA NIC
Application
FastWake shim layer
libibverbs
FastWake daemon
Kernel
ib_uverbs/core
switch_to() syscall
CQ-EQ remap
Comp channel
Per-core
polling threads
Compatible with existing RDMA applications.
  Only need an LD_PRELOAD library as a shim layer.
Compatible with existing OS.
  Update OFED kernel modules to shorten thread wake-up path and implement CQ-to-EQ remapping.
  Add a switch_to(pid) system call for direct context switch.
Compatible with existing RDMA NIC hardware.

## Slide 15: Evaluation – Latency (x86)
Dispatcher approach: reduce RDMA latency by 65%~83% on x86 at the cost of high power utilization.
Interrupt approach: reduce RDMA latency by 26%~64% on x86.

## Slide 16: Evaluation – Latency (ARM)
Dispatcher approach: reduce RDMA latency by 64%~78% on ARM at the cost of high power utilization.
Interrupt approach: reduce RDMA latency by 25%~54% on ARM.

## Slide 17: Comparing dispatcher and interrupt approaches of FastWake

## Slide 18: FastWake can also reduce IPC latency
IPC = Inter-Process Communication

## Slide 19: Conclusion
Data center networking and storage hardware are entering an age of microsecond-scale latency.
  Current CPU hardware and OS cannot hide this latency.
FastWake proposes two approaches with commodity NIC, OS and applications:
  Observation 1 – context switch is much faster than process scheduling.
    Solution 1 – build a per-core dispatcher thread and fast context switch to fully remove the interrupt overheads.
      Reduce RDMA latency by 65%~83% on x86 and 64%~78% on ARM.
      Only 0.4us (20%) higher than polling mode.
  Observation 2 – interrupt core affinity is crucial for performance.
    Solution 2 – a power-saving approach to reduce interrupt latency by ensuring interrupt core affinity and shortening kernel path.
      Reduce RDMA latency by 26%~64% on x86 and 25%~54% on ARM.
We expect future work to evaluate FastWake on real applications.
“The Killer Microseconds” is still an open problem.

## Slide 20: Thanks!
Q&A
Welcome to join/collaborate with Computer and Network Protocol Lab, Huawei.