## Slide 1: Memory Efficient Loss Recovery for Hardware-based Transport in Datacenter
Yuanwei Lu1,2, Guo Chen2, Zhenyuan Ruan1,2,
Wencong Xiao2,3, Bojie Li1,2, Jiansong Zhang2,
Yongqiang Xiong2, Peng Cheng2, Enhong Chen1
1USTC, 2Microsoft Research, 3BUAA

## Slide 2: Existing Hardware-based Transports
RDMA (RoCEv2)
High throughput, low latency and zero-cpu overhead
Go-back-N, PFC required
Light-weight Transport Layer (LTL)[1]
Inter-FPGA communication
Go-back-N, PFC required
[1] Adrian M Caulfield, et al. A cloud-scale acceleration architecture. MICRO 2016.

## Slide 3: Loss is Not Uncommon in DCs
Loss Sources
Congestion loss: can be removed by PFC
Failure loss: hard to be mitigated at large scale
Statistics from real DCs
A persistent 0.2% silent random drop which lasts for 2 days [2]
Loss ratio of some network switch can be up to 2% [2]
[2] Chuanxiong Guo, et al. Pingmesh: A large-scale system for data center network latency measurement and analysis. ACM SIGCOMM 2015

## Slide 4: Inefficient Loss Recovery
Go-Back-N
Tput drops to near zero when loss ratio is >0.1%

## Slide 5: How can we do better?
SACK TCP: state of the art loss recovery
Recover multiple losses within a sending window
Performs well under even high packet loss ratio, e.g. 1%
Question: can we extend selective retransmission to hardware-based transport?
Answer: MELO
Memory-Efficient LOss recovery
Implements Selective Retransmission for hardware transport

## Slide 6: Challenges
Hardware on-chip memory is limited
On-chip memory is usually a cache for off-chip memory
Swapping between on-chip and off-chip is expensive
Figure borrowed from: Anuj Kalia, et al. Design Guidelines for High Performance RDMA Systems. ATC 2016
Loss recovery for hardware transport should be on-chip memory-efficient

## Slide 7: Extra Memory is Required
#1: Re-ordering buffer is required to store loss induced out-of-order data
#2: Meta data is required for tracking out-of-order packets

## Slide 8: Challenge #1: Re-Ordering Buffer
The necessity of re-ordering buffer
RDMA requires in-order message placement
LTL requires in-order packet delivery
Size of out-of-order data
BDP: 100G * 100us ~ 1.25MB
Too much for on-chip memory
5
4
2
1
3
X
Flag
5
4
2
1
3
Read 3  ERROR
A re-ordering buffer is required before placing out-of-order data into app buffer
Ready

## Slide 9: Challenge #2: Meta Data
Selective retransmission bitmap size
BDP: 100G * 100us (1KB MTU) ~ 150B
Too much for on-chip memory: Mellanox CX3 Pro NIC, per-connection transport states is 248B
A per-connection bitmap would take too much on-chip memory

## Slide 10: MELO
Separate data and meta data storage
Re-ordering buffer in off-chip memory
Off-chip memory is large in size, usually GBs
Meta data in on-chip memory
On-chip memory is fast for frequent query and update
A shared bits pool structure to reduce on-chip meta data size

## Slide 11: Off-Chip Re-Ordering Buffer
Off-chip memory is usually GBs
A BDP worth of buffer is allocated to each connection
Buffer base address is stored in on-chip memory
An extra copy is required
For RDMA, trade some CPU for re-ordering buffer
For LTL, FPGA will perform the copy

## Slide 12: On-Chip Shared Bits Pool
Intuition
The bitmap of all connections is not fully occupied simultaneously
The total size of occupied bits is bounded by ingress bandwidth, O(n)  O(1)
… …
Ingress Bandwidth is Bottleneck
Instead of per-connection bitmap, we can use a shared bits pool

## Slide 13: Shared Bits Pool Management
Bits pool is divided into equal sized blocks
Eliminate external fragmentation
Allocation unit: 1 Byte, minimize internal fragmentation
Linked List: blocks linked into bitmap
A stack for maintaining available blocks
Blocks are allocated/returned from/to the top of the stack
Management overhead: 2 * Bits_Pool_Size
In total 23B extra data for each connection

## Slide 14: Shared Bits Pool Animation
...
Available Stack
0
1
2
127
avail_ptr
Connection #1
Connection #2
...
0
1
2
127
nxt
nxt
nxt
nxt
...
Bits Pool

## Slide 15: Access Pattern to Bitmap
Linked list is not friendly for random access
Fortunately, access pattern is not random
RCV.HIGH: new data
RCV.NXT: retransmission data
Other parts: out-of-order retransmission data  ignore and drop

## Slide 16: Evaluation
Setup
NS3: integrate MELO into DCQCN
Topology
Leaf-spine topology
40G-100G
RTT: 16us
MTU: 1KB
Bits Pool Size: 1Kb
Loss
Random loss at L0

## Slide 17: Preliminary Results
Throughput: 2.14X under 0.1% loss ratio
Tail Latency: 2.11X ~ 3.22X reduced

## Slide 18: Micro Benchmarks
CPU overhead: 30% core at 0.2% loss ratio
Bits pool usage: always < 100%
Interesting results: more concurrent connections leads to lower bits pool usage

## Slide 19: Future Implementation
FPGA implementation
FPGA captures all the outgoing/incoming traffic sequence number
Implements MELO
FPGA with MELO can deployed in DC to enhance RDMA NIC loss recovery
Plug in and play

## Slide 20: Future Work
Further Optimization
Consecutive 1s or 0s can be compressed
Remove PFC
MELO + end-to-end congestion control  remove PFC?

## Slide 21: Conclusion
MELO implements Selective Retransmission for hardware-based transport
MELO architecturally separates data and meta data storage
MELO leverages a shared bits pool structure to reduce on-chip memory size

## Slide 22: Thank you!

## Slide 23: Q& A

## Slide 24: Backup slides