## Slide 1: Towards SmartNICs in Data Center Systems
Bojie Li
Computer Network and Protocol Lab, Huawei

## Slide 2: Thanks
Thank the ACM China Doctoral Dissertation Award committee and the ACM ChinaSys Doctoral Dissertation Award committee for nominating me for the award.
Thank my advisors Prof. Enhong Chen, Prof. Lintao Zhang, and Prof. Kun Tan for the guidance during my joint Ph.D. program at USTC and MSRA (2014-2019).
Thank all collaborators of my research projects.

## Slide 3
Source: There’s plenty of room at the Top: What will drive computer performance after Moore’s law?
There’s plenty of room at the Top
The miniaturization of semiconductor transistors has driven the growth in computer performance for more than 50 years.
  There’s plenty of room at the Bottom – Richard Feynman, 1959.
As miniaturization approaches its limits, bringing an end to Moore’s law, performance gains will need to come from software, algorithms, and hardware.

## Slide 4: Network & storage still follow Moore’s Law
Chart: 
| 2010 | 2012 | 2014 | 2016 | 2018 | 2020
Network | 1 | 10 | 10 | 40 | 50 | 100
Storage | 0.4 | 8 | 8 | 32 | 32 | 128
LOG SCALE
Moore’s Law (2x per 1.5 years)
Throughput (Gbps)
HDD, 40 MB/s
SATA SSD, 1 GB/s
NVMe SSD, 4 GB/s
NVMM, 16 GB/s
1 GbE
10 GbE
40 GbE
50 GbE
100 GbE
Estimated Year of Deployment

## Slide 5: Challenges for software network functions
Limited processing capacity
  Number of CPU cores needed for 40 Gbps line rate
Inflated and unstable latency
  Add tens of microseconds to milliseconds latency to data plane
  Latency may grow to milliseconds under high load
  1 ms occasional delay would violate SLA (e.g., trading services)
Network function | Implementation | 1500B pkt @ 40 Gbps (normal case) | 64B pkt @ 40 Gbps (worst-case estimate)
NVGRE tunnel encapsulation | Hyper-V virtual switch | 5 | 100
Firewall (8K rules) | Linux iptables | 21 | 480
Notes: Second, software network functions have inflated and unstable latency.
A software-based network function adds tens of microseconds to milliseconds latency to the data plane.
When the load is high, this latency may grow to several milliseconds.
However, an occasional delay of one millisecond would already violate the service level agreement for delay sensitive applications.

## Slide 6: FPGAs in the cloud
FPGA-based SmartNIC
  Bump-in-the-wire processing between NIC and ToR switch[1]
Why FPGA?
  Massive parallelism
  - Millions of logic elements Thousands of “cores” in parallel
  - Thousands of memory blocks TB/s memory bandwidth
  Low power consumption (~20W)
  General computing platform (vs. GPU, NP) to accelerate various cloud services
  Mature technology with a reasonable price
[1] Albert Greenberg, SIGCOMM’15 keynote (also the image source)
Notes: There are several reasons for choosing FPGA as the accelerator.
First, FPGA has massive parallelism.
It has millions of logic elements, which can build thousands of “cores” running in parallel.
FPGA also has thousands of memory blocks, which can produce terabytes per second aggregated memory bandwidth.
Second, FPGA has low power utilization.
Third, FPGA is a general computing platform to accelerate various cloud services, so the hardware investment can be amortized by multiple applications.
Finally, FPGA is a mature technology with reasonable price in recent years.

## Slide 7: 1. Network Function Acceleration
Hypervisor
VM1
VM2
VM3
Compute Node
Virt Disk
Virt Disk
Virt Net
NIC
Network Node
Data Structure
NIC
Storage Node
DDR / Flash
Data center network
App
OS
App
OS
App
OS
DDR / Flash
Programmable
NIC
VNF Data Plane
VNF Control Plane

## Slide 8: ClickNP: Highly Flexible and High Performance Network Processing with Reconfigurable Hardware
Bojie Li1,2, Kun Tan1, Layong (Larry) Luo1, Yanqing Peng1,3, Renqian Luo1,2, Ningyi Xu1, Yongqiang Xiong1, Peng Cheng1, Enhong Chen2
1Microsoft Research, 2USTC, 3SJTU
SIGCOMM’16

## Slide 9: FPGA challenge: Programmability
Hardware description language (HDL): push many software developers away
PCIe Core
DMA Engine
Ahhhhhhhhhhhh!
always @ (posedge SYSCLK or negedge RST_B)
begin
if(!RST_B)
DMA_TX_DATA <= `UD 8'hff;
else
DMA_TX_DATA <= `UD DMA_TX_DATA_N;
end
//send: "hello world !"
always @ (posedge SYSCLK)
begin
if (rst) begin
dma_data <= 88’h0;
dma_valid <= 1’b0;
else
if (dma_start) begin
dma_data <= 88’h68656C6C6F20776F726C64;
dma_valid <= 1’b1;
end
else begin
dma_data <= 88’h0;
dma_valid <= 1’b0;
end
end
end
Notes: The main challenge to use FPGA is programmability.
Conventionally, FPGA is programmed with low-level hardware description languages, such as Verilog and VHDL.
This example shows a HelloWorld program in Verilog.
To print a HelloWorld string on the screen, we first need to translate the string into ASCII codes.
In order to send the codes to the host memory, we need to write a DMA engine.
The DMA engine needs to call a PCI express IP core, which requires reading three hundred pages of manual to understand the interface.
The difficulty of hardware description languages have pushed many software developers away for years.

## Slide 10: Project ClickNP
Making FPGA accessible to software developers
Flexibility: fully programmable using high-level language
Modularized: Click abstractions familiar to software developers; easy code reuse
High performance: high throughput; microsecond-scale latency
Joint CPU/FPGA packet processing: FPGA is no panacea; fine-grained processing separation
Notes: In this work, we present ClickNP, a platform to make FPGA accessible to software developers.
We have several design goals.
First, the platform should be fully programmable using high-level languages.
Second, the platform should have a modular architecture familiar to software developers. In particular, we choose abstractions similar to the Click modular router for easy code reuse.
Third, the platform should provide high performance, both in terms of throughput and latency.
Finally, the platform should support joint CPU and FPGA packet processing. That’s because FPGA is not suitable for every kind of workload. We should support fine-grained processing separation between CPU and FPGA. This requires high performance and low latency communication between CPU and FPGA.

## Slide 11: Programming model
as if programming on a multi-core processor
A
mem
B
mem
C
mem
cores (elements) running in parallel
communicate via channels, not shared memory
Notes: ClickNP provides a modular programming model similar to the Click modular router.
Therefore, programming in ClickNP is much like programming on a multi-core processor.
There is one important difference, though.
In conventional multi-core processing, threads communicate via shared memory.
However, In ClickNP, the cores communicate via channels instead of shared memory.
Channel-based communication is more efficient in FPGA compared to shared global memory, because the shared global memory would be the bottleneck.

## Slide 12: Element: single-threaded core
input channels
Process handler
signal/control from host
output channels
states
Signal handler
(interrupt)
(I/O)
(I/O)
(reg/mem)
(main thread)
(ISR)
Notes: In ClickNP, the basic processing module is called an element, which resembles a single-threaded core.
Each element has the following components.
First, a set of local states that are only accessible inside the element.
Second, input and output channels to communicate with other elements.
Third, process handler, which is the main thread to read input channels, do processing and write to output channels in an infinite loop.
Finally, signal handler, which receives and processes commands from the manager thread in host program running on CPU. Signals resemble interrupts in CPU.

## Slide 13: Architecture
Catapult shell
ClickNP
FPGA
Host
Catapult PCIe Driver
ClickNP library
ClickNP host process
Mgr thrd
Worker thrd
ClickNP elements
ClickNP host mgr
ClickNP compiler
vendor libs
vendor HLS
PCIe I/O channel
Cross-platform toolchain
Altera OpenCL / Vivado HLS
Visual Studio / GCC
vendor specific runtime
ClickNP script
C compiler
Verilog
Intermediate C files
Notes: In runtime environment, the Catapult shell is the operating system on the FPGA, which was developed by the Microsoft Catapult team.
The Catapult shell provides resource abstractions to the ClickNP application logic.
On host side, the ClickNP library provides PCIe I/O channel abstraction to the CPU elements, and enables the host program to communicate with FPGA elements via signals.

## Slide 14: Case study: L4 load balancer
  Performance
  10M new flows per second
  51Mpps for 8K flows
  11Mpps for 32M flows
  4us stable latency
Notes: The L4 load balancer can sustain 10 million new connections per second.
The bottleneck is DRAM random access, instead of PCIe I/O channel to communicate with the nexthop allocation element on CPU.
When the number of concurrent flows is small, the throughput can achieve 50 million packets per second.
When the number of concurrent flows exceed flow cache size, the throughput begins to decrease due to cache miss.
The L4 load balancer also has microsecond-scale stable latency.

## Slide 15: 2. Data Structure Acceleration
Hypervisor
VM1
VM2
VM3
Compute Node
Virt Disk
Virt Disk
Virt Net
NIC
Network Node
Storage Node
Data center network
App
OS
App
OS
App
OS
DDR / Flash
Programmable
NIC
VNF Data Plane
VNF Control Plane
DDR / Flash
Programmable
NIC
Data Structure Data Plane
Data Structure Control Plane

## Slide 16: KV-Direct: High-Performance In-Memory Key-Value Store with Programmable NIC
Bojie Li1,2 Zhenyuan Ruan1,3 Wencong Xiao1,4 Yuanwei Lu1,2 Yongqiang Xiong1 Andrew Putnam1 Enhong Chen2
Lintao Zhang1
1Microsoft Research 2USTC 3UCLA 4Beihang University
SOSP ’17
Notes: Thanks Adita for the introduction.
Hello everyone, I’m Bojie Li, a fourth year PhD student in a joint PhD program of USTC and Microsoft Research.
In this session we have seen two wonderful works, Eris and NetCache to use in-network processing with dataplane programmable switches to accelerate systems.
Now I will show programmable NICs can also be very useful in accelerating datacenter workloads.
Our KV-Direct work is done during internship in Microsoft Research Asia with my colleagues. Zhenyuan Ruan and me are co-first authors who design and implement this system together.

## Slide 17: Key-Value Store in Data Centers
Web Cache
Shared Data Structure
Recent Tweets
User ID
SQL
Query result
Key
Value
Session
Browser cookies
Graph node
Feature
Weight
Key
Value
Shard
Sequence number
List of edges
More demanding workload
Notes: In recent years, key-value store goes beyond object caching and becomes an infrastructure service to store shared data structure in a distributed system.
Examples include parameter servers in machine learning, graph computing engine and sequencers for distributed transactions, as the Eris paper in this session just said.
Shared data structure stores demands more performance compared to web cache.

## Slide 18: Key-Value Store Architectures
Software (Kernel Bypass)
One-sided RDMA
KV-Direct FPGA + NIC
Offload KV processing on CPU to Programmable NIC
Software (Kernel TCP/IP)
Leverage the SmartNIC to access remote data structures in host memory without involving CPU
Key-value store is only an example
Bottleneck: OS TCP/IP Stack
Bottleneck: CPU random memory access & KV processing
Bottlenecks:
1. Multiple round-trips per KV op
2. Synchronization among writes
Notes: We propose KV-Direct to offload KV processing on CPU to programmable NIC.
The name of KV-Direct means that the NIC directly fetches data and applies updates in the host memory to serve KV requests, completely bypassing server CPU.

## Slide 19: Performance Challenges
ToR switch
Host DRAM (256 GB)
PCIe Gen3 x16 DMA
40 GbE
FPGA
CPU
NIC
Reconfigurable NIC
On-board DRAM (4 GB)
13 GB/s
120 Mops
Header overhead and limited parallelism: Be frugal on memory accesses
Notes: First, our PCIe interface between FPGA and host memory has limited throughput.
There is something worse. PCIe transport layer packets has header overhead, and the PCIe IP core in our FPGA has limited parallelism, which limits our PCIe throughput to 120 million operations per second.
So we need to be frugal on memory accesses.

## Slide 20: Performance Challenges
ToR switch
Host DRAM (256 GB)
PCIe Gen3 x16 DMA
40 GbE
FPGA
CPU
NIC
Reconfigurable NIC
On-board DRAM (4 GB)
1us delay
120 Mops
Atomic operations have dependency:
PCIe latency hiding
Notes: Second, the PCIe bus has delay of nearly 1 microsecond, due to additional delay in the PCIe IP core in our FPGA.
When atomic operations operate on the same key, they depend on the result of each other and needs to executed one by one.
Therefore, we need to hide the PCIe latency, otherwise the throughput will degrade to 1 million operations per second.

## Slide 21: KV-Direct Performance
1.22 billion KV op/s
357 watts power
Notes: This photo is our test server with 10 programmable NICs, two Xeon E5 processors and 128 Gigabytes of memory.
Each programmable NIC is connected to the motherboard via 8 lanes of PCIe Gen3, so the 10 NICs saturate the 80 PCIe lanes from two Xeon E5 processors.
(click) With 10 programmable NICs, KV-Direct achieves 1.2 billion key-value operations per second with less than 400 watts of power consumption, setting a new milestone for general purpose key-value stores.

## Slide 22: We expect future SmartNICs to tightly integrate with host CPU
Core 1
Core 2
Core 3
NIC
Mem controller
DDR
PCIe RC
PCIe
Core 1
Core 2
Core 3
NIC
Mem controller
DDR
SoC
Recall: why we need to be frugal on memory accesses? Why we need to hide PCIe latency?

## Slide 23: 3. Acceleration of OS Communication Primitives
Hypervisor
VM1
VM2
VM3
Compute Node
Programmable
NIC
Data Center Network
vNIC1
vNIC2
vNIC3
Virt Disk
Virt Net
App
OS (Socket)
App
App
Mem / Flash
Communication Protocol
Network Node
Storage Node
Programmable
NIC
VNF Data Plane
VNF Control Plane
DDR / Flash
Programmable
NIC
Data Structure Data Plane
Data Structure Control Plane
OS (Socket)
OS (Socket)

## Slide 24: SocksDirect: Datacenter Sockets can be Fast and Compatible
Bojie Li*1,2 Tianyi Cui*3 Zibo Wang1,2 Wei Bai1 Lintao Zhang1
1Microsoft Research 2USTC 3University of Washington
* Co-first authors
SIGCOMM ‘19

## Slide 25: Socket: a Performance Bottleneck
Socket syscall time >> user application time
Chart: 
| Lighttpd HTTP Server | Nginx HTTP Load Balancer | Redis Key-Value Store | NSC DNS Server
Kernel time | 0.78 | 0.77 | 0.87 | 0.92
User application time | 0.22 | 0.23 | 0.13 | 0.08
Socket latency >> hardware transport latency
Chart: 
| Intra-host (vs. shared memory) | Inter-host (vs. RDMA)
shared memory (SHM) / RDMA | 0.25 | 1.6
Linux Socket | 11 | 30
Notes: Traditionally, sockets are implemented in the OS kernel. We all know that kernel socket is very slow. To show this point, we profile several popular applications in data centers. We can see that 70% to 90% of CPU time is used in OS kernel, which means it is handling the socket system calls. If we could eliminate the overhead of OS kernel and all CPU time can be utilized by the user space application, the application throughput will improve by several times.
Next we look at the latency, and the problem is more severe than throughput. For communication between two directly connected servers, socket latency is 17x of RDMA. For intra-host communication, socket latency is 40x of shared memory queue. In this work, we try to answer one question: is this socket overhead an intrinsic property of the socket abstraction, or we can do something to eliminate the socket overhead?

## Slide 26: High Performance Socket Systems
User App
User App
User App
Kernel VFS
Host 1
Host 2
Kernel Optimization
FastSocket, Megapipe, StackMap…
User-space TCP/IP
Offload to RDMA NIC
IX, Arrakis, SandStorm, mTCP, LibVMA, OpenOnload…
Rsocket, SDP, FreeFlow…
User App
User-space VFS
User App
User-space VFS
Host 1
TCP/IP
TCP/IP
User App
Host 2
Kernel TCP/IP
NIC packet API
User-space TCP/IP
User-space TCP/IP
NIC packet API
NIC packet API
Kernel
NIC packet API
User-space Stack
User App
User-space VFS
User App
User-space VFS
Host 1
RDMA
User App
Host 2
NIC RDMA API Hardware-based Transport
NIC RDMA API
User-space VFS
Notes: There have been extensive research to improve the performance of socket systems.
The first category is to optimize the kernel. A socket stack basically divides into three layers. The first layer is the virtual file system, VFS, because each socket connection is regarded as a file in Linux, and a file descriptor is mapped for the socket. The second layer is the kernel TCP/IP stack that provides the transport function. The third layer is the hardware interface layer. Linux kernel uses a packet API.
The second category is to implement the VFS abstraction and TCP/IP transport in the user space. It not only move the kernel functions into user space, but also greatly simplify the functions, for example, use polling to avoid the interrupt and process scheduling overheads.
The third category is to offload the transport to the NIC. Here we recall some history of hardware-based transports. TCP offload is not a new thing. In 1990s, there has been Ethernet cards that

## Slide 27: Application Performance
Nginx HTTP server request latency
Notes: Nginx HTTP server between two hosts: small HTTP messages, 5x lower than Linux. For large message, 13x lower than Linux due to zero copy.

## Slide 28: The Future of SmartNICs
Data center as a computer
SmartNICs build the hardware acceleration plane
Web search ranking
Traditional software (CPU) server plane
Hardware acceleration plane
Web search ranking
Deep neural networks
SDN offload
SQL
UPI
DRAM
DRAM
GPU/NPU
CPU
2
ToR
CPU
Network
Program-mable NIC
The best way to predict the future is to create it.
Fast Bus

## Slide 29: Disaggregated Pool of Tiered Memory
Towards memory disaggregation in a cluster
  Motivation 1: 40% hardware cost of cloud servers is DDR. VM memory usage is highly unbalanced, and 40% provisioned memory capacity is unused. Borrowing unused memory from other nodes in the cluster can expand memory capacity.
  Motivation 2: Big data and database applications require PB-scale storage, which needs to store large data structures in a memory cluster.
Towards disaggregated pool of tiered memory
  DDR/Optane/Flash are different classes of storage with different capacity, price, and persistence.
  DDR should be a performance layer holding the hot data.

## Slide 30: Disaggregated Pool of Tiered Memory
Problem: latency of remote memory and Flash storage is much higher than local DDR access!
  One way: can we build a (co-)processor with hardware multithreading to hide the latency of slow memory accesses?
  The other way: can we move computation to data?
CPU
DDR
Flash
Host 1
CPU
DDR
Flash
Host 2
CPU
DDR
Flash
Host 3
Network RTT = 3 us
Flash latency = 30 us
DDR latency = 0.1 us

## Slide 31: Heterogenous Data Access Methods
Compute at Client
Memory-mapped Load/Store
(CXL, Gen-Z, etc.)
Asynchronous Read/Write
(one-sided RDMA)
Compute at Server
(Home Node of Data)
SmartNIC Offloading
In-Network Computation
RPC on CPU
Load/Store: low overhead per operation, but synchronous; may have cache and buffer
Read/Write: high overhead per operation, but each op can transfer a large block, and many ops can work in parallel
Switch: high throughput but low programmability and buffer size
SmartNIC: high parallelism but high PCIe latency and low buffer size
RPC on CPU: close to memory, easy to program but high cost
How to choose data access methods?
Can we have a unified programming framework?
Notes: Now we have heterogenous methods to access a piece of remote data in data center networks. Traditionally, the only way to access remote data is by executing RPC on the remote CPU. Then we have RDMA technology to directly copy the data to local buffer and do computation. If the data structure is complicated, we may need multiple network round-trips to RDMA the data. But because it removes the cost to invoke an RPC on the remote CPU, which is mainly the TCP/IP and RPC protocol stack, the overall performance may be still higher. Next we have smartNIC offloading and in-network computation. SmartNIC is high parallelism but its main drawback is high PCIe latency and low on-chip buffer size. Network switches also have low buffer size but high throughput. In the next a few years we will have memory-mapped load/store over network, which has lower per-operation overhead compared to reads and writes, but each operation only accesses a cache line of data. In summary, we have a wide spectrum of data access methods, and we need some way to choose among them.

## Slide 32: Improving Data Locality
In a disaggregated pool of tiered memory:
  When using remote memory to expand local memory, hot data should be in local memory.
  Hot data in the cluster should be in DDR rather than slow storage media.
Open question: how to do data hotness measurement and migration?
  Current approach: LRU, LFU, random…
  How to choose among them? See paper: Adaptive Page Migration Policy with Huge Pages in Tiered Memory Systems.
  Can we use AI to predict data hotness?
Can we cache hot data at clients?
  How to maintain cache coherence among clients and server?

## Slide 33: Conclusion
Infrastructure services in data centers mainly use software processing on general processors, whose performance lags behind networking, storage and customized computing hardware.
To provide high performance and flexibility, recent years witnessed large scale deployment of programmable NICs (SmartNICs) in data centers.
We use SmartNICs to offload network functions, remote data structures, and OS communication primitives.
We expect future SmartNICs will be tightly integrated with host CPU, support programmable offloading, and build the data plane for disaggregated pool of tiered memory.

## Slide 34
Thanks
Ad: Welcome to Computer Network and Protocol Lab in Huawei.
We work on next-generation data center interconnects and networked systems.
Contact Info:
WeChat: bojustc (or 15011272877)
E-mail: bojieli@gmail.com
Homepage: https://ring0.me (slides will be available on my homepage)