## Slide 1: Towards SmartNICs in Data Center Systems
Bojie Li
Computer Network and Protocol Lab, Huawei

## Slide 2: Outline
Why SmartNICs
SmartNIC applications
  ClickNP: highly flexible and high performance network processing with FPGA
  KV-Direct: a high-performance in-memory key-value store with FPGA
  SocksDirect: high performance socket communication
  DUA: making data center resources available to FPGA
The future of SmartNIC architecture

## Slide 3: There’s plenty of room at the Bottom
Source: EXPERIMENT ON MULTI BLEND BIODIESEL USING JATROPHA AND PONGAMIA BIODIESEL ON SINGLE CYLINDER DIESEL ENGINE WITH BASE LINE OF DIESEL FUEL
Source: CMOS Scaling Trends and Beyond, IEEE Micro 2017
– Richard Feynman, 1959
The miniaturization of semiconductor transistors has driven the growth in computer performance for more than 50 years.

## Slide 4
Source: There’s plenty of room at the Top: What will drive computer performance after Moore’s law?
There’s plenty of room at the Top
As miniaturization approaches its limits, bringing an end to Moore’s law, performance gains will need to come from software, algorithms, and hardware.

## Slide 5: Accelerators still follow Moore’s Law
Chart: Estimated Year of Deployment
| 2015 | 2016 | 2015 | 2017 | 2016 | 2017 | 2017 | 2019 | 2017 | 2017 | 2018 | 2018 | 2018
In Deployment | 8.5714 | 9.0909
In Deployment | 1226.6667 | 281.25
In Deployment | 29.1333 | 70.6667 | 188 | 400
In Deployment | 69.3333 | 200 | 240 | 440 | 640 | 1280
LOG SCALE
Note: assumes power consumption of 160W/TPU2 chip (not confirmed)
Moore’s Law (2x per 1.5 years)
Still working for specialized hardware
CPU: End of frequency & Dennard scaling
Notes: Although many people are saying the Moore’s law is ending, it is about the CPU. The end of frequency and Dennard scaling has caused the performance of CPUs to improve slowly in recent years.
On the other hand, accelerators are

## Slide 6: Network & storage follow Moore’s Law
Chart: 
| 2010 | 2012 | 2014 | 2016 | 2018 | 2020
Network | 1 | 10 | 10 | 40 | 50 | 100
Storage | 0.4 | 8 | 8 | 32 | 32 | 128
LOG SCALE
Moore’s Law (2x per 1.5 years)
Throughput (Gbps)
HDD, 40 MB/s
SATA SSD, 1 GB/s
NVMe SSD, 4 GB/s
NVMM, 16 GB/s
1 GbE
10 GbE
40 GbE
50 GbE
100 GbE
Estimated Year of Deployment

## Slide 7: How to waste a fast datacenter network
Source: Attack of the Killer Microseconds, Communications of the ACM, 2017

## Slide 8: FPGAs in the cloud
FPGA-based SmartNIC
  Bump-in-the-wire processing between NIC and ToR switch[1]
Why FPGA?
  Massive parallelism
  - Millions of logic elements Thousands of “cores” in parallel
  - Thousands of memory blocks TB/s memory bandwidth
  Low power consumption (~20W)
  General computing platform (vs. GPU, NP) to accelerate various cloud services
  Mature technology with a reasonable price
[1] Albert Greenberg, SIGCOMM’15 keynote (also the image source)
Notes: There are several reasons for choosing FPGA as the accelerator.
First, FPGA has massive parallelism.
It has millions of logic elements, which can build thousands of “cores” running in parallel.
FPGA also has thousands of memory blocks, which can produce terabytes per second aggregated memory bandwidth.
Second, FPGA has low power utilization.
Third, FPGA is a general computing platform to accelerate various cloud services, so the hardware investment can be amortized by multiple applications.
Finally, FPGA is a mature technology with reasonable price in recent years.

## Slide 9: Outline
Why SmartNICs
SmartNIC applications
  ClickNP: highly flexible and high performance network processing with FPGA
  KV-Direct: a high-performance in-memory key-value store with FPGA
  SocksDirect: high performance socket communication
  DUA: making data center resources available to FPGA
The future of SmartNIC architecture

## Slide 10: Cloud Datacenter Architecture
Hypervisor
VM1
VM2
VM3
Compute Node
Virt Disk
Virt Disk
Virt Net
NIC
Virtual Net Func
NIC
Network Node
Data Structure
NIC
Storage Node
DDR / Flash
Data center network
Bottlenecks at compute, network, and storage nodes
App
OS
App
OS
App
OS
DDR / Flash

## Slide 11: 1.1. Virtual Network Acceleration
Hypervisor
VM1
VM2
VM3
Compute Node
Programmable NIC
Data Center Network
vNIC1
vNIC2
vNIC3
Virt Net
App
OS
App
OS
App
OS
DDR / Flash
Virt Disk
Virt Disk
Virtual Net Func
NIC
Network Node
Data Structure
NIC
Storage Node
DDR / Flash

## Slide 12: 1.2. Network Function Acceleration
Hypervisor
VM1
VM2
VM3
Compute Node
Virt Disk
Virt Disk
Virt Net
NIC
Network Node
Data Structure
NIC
Storage Node
DDR / Flash
Data center network
App
OS
App
OS
App
OS
DDR / Flash
Programmable
NIC
VNF Data Plane
VNF Control Plane

## Slide 13: ClickNP: Highly Flexible and High Performance Network Processing with Reconfigurable Hardware
Bojie Li1,2, Kun Tan1, Layong (Larry) Luo1, Yanqing Peng1,3, Renqian Luo1,2, Ningyi Xu1, Yongqiang Xiong1, Peng Cheng1, Enhong Chen2
1Microsoft Research, 2USTC, 3SJTU
SIGCOMM’16

## Slide 14: Scale-up challenges for software NF
Limited processing capacity
  Number of CPU cores needed for 40 Gbps line rate
Network function | Implementation | 1500B pkt @ 40 Gbps (normal case) | 64B pkt @ 40 Gbps (worst-case estimate)
NVGRE tunnel encapsulation | Hyper-V virtual switch | 5 | 100
Firewall (8K rules) | Linux iptables | 21 | 480
Notes: However, there are two major challenges for software network functions.
First, software network functions have limited processing capacity.
For example, for NVGRE tunnel encapsulation, the virtual switch requires 5 CPU cores to sustain 40 gigabit line rate.
In the worst case, when all the packets are tiny, it requires as many as 100 cores to sustain line rate.
This is only a roughly estimation, but the order of magnitude should make sense.

## Slide 15: Scale-up challenges for software NF
Limited processing capacity
  Number of CPU cores needed for 40 Gbps line rate
Inflated and unstable latency
  Add tens of microseconds to milliseconds latency to data plane
  Latency may grow to milliseconds under high load
  1 ms occasional delay would violate SLA (e.g., trading services)
Network function | Implementation | 1500B pkt @ 40 Gbps (normal case) | 64B pkt @ 40 Gbps (worst-case estimate)
NVGRE tunnel encapsulation | Hyper-V virtual switch | 5 | 100
Firewall (8K rules) | Linux iptables | 21 | 480
Notes: Second, software network functions have inflated and unstable latency.
A software-based network function adds tens of microseconds to milliseconds latency to the data plane.
When the load is high, this latency may grow to several milliseconds.
However, an occasional delay of one millisecond would already violate the service level agreement for delay sensitive applications.

## Slide 16: FPGA challenge: Programmability
Hardware description language (HDL): push many software developers away
PCIe Core
DMA Engine
Ahhhhhhhhhhhh!
always @ (posedge SYSCLK or negedge RST_B)
begin
if(!RST_B)
DMA_TX_DATA <= `UD 8'hff;
else
DMA_TX_DATA <= `UD DMA_TX_DATA_N;
end
//send: "hello world !"
always @ (posedge SYSCLK)
begin
if (rst) begin
dma_data <= 88’h0;
dma_valid <= 1’b0;
else
if (dma_start) begin
dma_data <= 88’h68656C6C6F20776F726C64;
dma_valid <= 1’b1;
end
else begin
dma_data <= 88’h0;
dma_valid <= 1’b0;
end
end
end
Notes: The main challenge to use FPGA is programmability.
Conventionally, FPGA is programmed with low-level hardware description languages, such as Verilog and VHDL.
This example shows a HelloWorld program in Verilog.
To print a HelloWorld string on the screen, we first need to translate the string into ASCII codes.
In order to send the codes to the host memory, we need to write a DMA engine.
The DMA engine needs to call a PCI express IP core, which requires reading three hundred pages of manual to understand the interface.
The difficulty of hardware description languages have pushed many software developers away for years.

## Slide 17: Project ClickNP
Making FPGA accessible to software developers
Flexibility: fully programmable using high-level language
Modularized: Click abstractions familiar to software developers; easy code reuse
High performance: high throughput; microsecond-scale latency
Joint CPU/FPGA packet processing: FPGA is no panacea; fine-grained processing separation
Notes: In this work, we present ClickNP, a platform to make FPGA accessible to software developers.
We have several design goals.
First, the platform should be fully programmable using high-level languages.
Second, the platform should have a modular architecture familiar to software developers. In particular, we choose abstractions similar to the Click modular router for easy code reuse.
Third, the platform should provide high performance, both in terms of throughput and latency.
Finally, the platform should support joint CPU and FPGA packet processing. That’s because FPGA is not suitable for every kind of workload. We should support fine-grained processing separation between CPU and FPGA. This requires high performance and low latency communication between CPU and FPGA.

## Slide 18: Programming model
as if programming on a multi-core processor
A
mem
B
mem
C
mem
cores (elements) running in parallel
communicate via channels, not shared memory
Notes: ClickNP provides a modular programming model similar to the Click modular router.
Therefore, programming in ClickNP is much like programming on a multi-core processor.
There is one important difference, though.
In conventional multi-core processing, threads communicate via shared memory.
However, In ClickNP, the cores communicate via channels instead of shared memory.
Channel-based communication is more efficient in FPGA compared to shared global memory, because the shared global memory would be the bottleneck.

## Slide 19: Element: single-threaded core
input channels
Process handler
signal/control from host
output channels
states
Signal handler
(interrupt)
(I/O)
(I/O)
(reg/mem)
(main thread)
(ISR)
Notes: In ClickNP, the basic processing module is called an element, which resembles a single-threaded core.
Each element has the following components.
First, a set of local states that are only accessible inside the element.
Second, input and output channels to communicate with other elements.
Third, process handler, which is the main thread to read input channels, do processing and write to output channels in an infinite loop.
Finally, signal handler, which receives and processes commands from the manager thread in host program running on CPU. Signals resemble interrupts in CPU.

## Slide 20: Architecture
Catapult shell
ClickNP
FPGA
Host
Catapult PCIe Driver
ClickNP library
ClickNP host process
Mgr thrd
Worker thrd
ClickNP elements
ClickNP host mgr
ClickNP compiler
vendor libs
vendor HLS
PCIe I/O channel
vendor specific runtime
ClickNP script
C compiler
Cross-platform toolchain
Altera OpenCL / Vivado HLS
Visual Studio / GCC
Intermediate C files
Verilog
Notes: Here we look at the architecture of the ClickNP toolchain.
A ClickNP program is divided into three parts, a set of ClickNP elements, a ClickNP script to define the connections among elements, and a ClickNP host manager program.

## Slide 21: Architecture
Catapult shell
ClickNP
FPGA
Host
Catapult PCIe Driver
ClickNP library
ClickNP host process
Mgr thrd
Worker thrd
ClickNP elements
ClickNP host mgr
ClickNP compiler
vendor libs
vendor HLS
PCIe I/O channel
vendor specific runtime
ClickNP script
C compiler
Cross-platform toolchain
Altera OpenCL / Vivado HLS
Visual Studio / GCC
Verilog
Intermediate C files
Notes: The ClickNP compiler first compiles the ClickNP program to intermediate C code.

## Slide 22: Architecture
Catapult shell
ClickNP
FPGA
Host
Catapult PCIe Driver
ClickNP library
ClickNP host process
Mgr thrd
Worker thrd
ClickNP elements
ClickNP host mgr
ClickNP compiler
vendor libs
vendor HLS
PCIe I/O channel
vendor specific runtime
ClickNP script
C compiler
Cross-platform toolchain
Altera OpenCL / Vivado HLS
Visual Studio / GCC
Verilog
Intermediate C files
Notes: Then we call a vendor HLS tool, for example Altera OpenCL or Vivado HLS, to compile the intermediate C code into Verilog code.

## Slide 23: Architecture
Catapult shell
ClickNP
FPGA
Host
Catapult PCIe Driver
ClickNP library
ClickNP host process
Mgr thrd
Worker thrd
ClickNP elements
ClickNP host mgr
ClickNP compiler
vendor libs
vendor HLS
PCIe I/O channel
vendor specific runtime
ClickNP script
C compiler
Cross-platform toolchain
Altera OpenCL / Vivado HLS
Visual Studio / GCC
Verilog
Intermediate C files
Notes: Finally we call the hardware synthesis toolchain to generate the FPGA bitstream.

## Slide 24: Architecture
Catapult shell
ClickNP
FPGA
Host
Catapult PCIe Driver
ClickNP library
ClickNP host process
Mgr thrd
Worker thrd
ClickNP elements
ClickNP host mgr
ClickNP compiler
vendor libs
vendor HLS
PCIe I/O channel
vendor specific runtime
ClickNP script
C compiler
Cross-platform toolchain
Altera OpenCL / Vivado HLS
Visual Studio / GCC
Verilog
Intermediate C files
Notes: And call a standard C compiler to compile the ClickNP host program.

## Slide 25: Architecture
Catapult shell
ClickNP
FPGA
Host
Catapult PCIe Driver
ClickNP library
ClickNP host process
Mgr thrd
Worker thrd
ClickNP elements
ClickNP host mgr
ClickNP compiler
vendor libs
vendor HLS
PCIe I/O channel
Cross-platform toolchain
Altera OpenCL / Vivado HLS
Visual Studio / GCC
vendor specific runtime
ClickNP script
C compiler
Verilog
Intermediate C files
Notes: In runtime environment, the Catapult shell is the operating system on the FPGA, which was developed by the Microsoft Catapult team.
The Catapult shell provides resource abstractions to the ClickNP application logic.
On host side, the ClickNP library provides PCIe I/O channel abstraction to the CPU elements, and enables the host program to communicate with FPGA elements via signals.

## Slide 26: Example: Packet logger
ClickNP Configuration:
from_tor
Count
Tee
to_tor
logger
FPGA
CPU
Notes: Here we look at an example network function, packet logger.
It receives packets from top-of-rack switch, counts number of packets in Count element, then makes a copy in Tee element.
One copy is forwarded back to ToR switch, the other copy is forwarded to a host element PktLogger running on CPU.
We can see that this PacketLogger needs only 5 lines of code for ClickNP configuration.

## Slide 27: Example: Packet logger
ClickNP Configuration:
Count element:
from_tor
Count
Tee
to_tor
logger
FPGA
CPU
Notes: Now we look at details of the Count element.
The first line of code shows that the Count element has one input channel and one output channel.
There is only one state variable, count, and initialized to zero.
In the handler, we first check whether or not the input channel has data to read. If so, we read a block of packet data from the input channel.
If the metadata indicates that it is start of packet, we increment the counter by one.
Finally we forward the data to the output port.
The signal handler simply writes the counter to a special structure called ClSignal, which is then returned to the manager thread in host program.

## Slide 28: Parallelizing in FPGA
Parallelism across elements
  Pipeline parallelism
  Data parallelism
Parallelism inside an element
  Minimize memory dependency
  Use registers
  Delayed write
  Memory scattering
  Balance pipeline stages
  Unroll loops
  Offload slow path to another element
Notes: Now we come to optimizations in ClickNP.
As we know, efficient FPGA code must utilize parallelism, which basically includes parallelism across elements and parallelism inside an element.
Due to time limitations, here I’m only going to discuss several of them. For the remaining ones, please refer to the paper.

## Slide 29: ClickNP element library
Nearly 200 elements
20% re-factored from Click modular router
Cover packet parsing, checksum, tunnel encap/decap, crypto, hash tables, prefix matching, packet scheduling, rate limiting…
Throughput: 200 Mpps / 100 Gbps
Mean delay: 0.19 us, max delay: 0.8 us
Mean LoC: 80, max LoC: 196
Element | Fmax (MHz) | Peak Throughput | Delay (cycles) | Resource LE % | Resource BRAM %
L4_Parser | 221.9 | 113.6 Gbps | 11 | 0.8% | 0.2%
IPChecksum | 226.8 | 116.1 Gbps | 18 | 2.3% | 1.3%
NVGRE_Encap | 221.8 | 113.6 Gbps | 9 | 1.5% | 0.6%
AES_CTR | 217.0 | 27.8 Gbps | 70 | 4.0% | 23.1%
SHA1 | 220.8 | 113.0 Gbps | 105 | 7.9% | 6.6%
CuckooHash | 209.7 | 209.7 Mpps | 38 | 2.0% | 65.5%
HashTCAM | 207.4 | 207.4 Mpps | 48 | 18.7% | 22.0%
LPM_Tree | 221.8 | 221.8 Mpps | 181 | 4.3% | 13.2%
SRPrioQueue | 214.5 | 214.5 Mpps | 41 | 2.6% | 0.6%
RateLimiter | 141.5 | 141.5 Mpps | 14 | 16.9% | 14.1%
Notes: We have built a ClickNP element library with nearly 200 elements.
About 20% of them are re-factored from Click modular router, and the remaining ones cover lots of network functions.
This table shows some common elements in the element library, which cover packet parsing, checksum, tunnel encapsulation, crypto, hash tables, prefix matching, packet scheduling and rate limiting.

## Slide 30: Case study: L4 load balancer
  Performance
  10M new flows per second
  51Mpps for 8K flows
  11Mpps for 32M flows
  4us stable latency
Notes: The L4 load balancer can sustain 10 million new connections per second.
The bottleneck is DRAM random access, instead of PCIe I/O channel to communicate with the nexthop allocation element on CPU.
When the number of concurrent flows is small, the throughput can achieve 50 million packets per second.
When the number of concurrent flows exceed flow cache size, the throughput begins to decrease due to cache miss.
The L4 load balancer also has microsecond-scale stable latency.

## Slide 31: Area cost
Overhead compared to hand-written Verilog
NetFPFA Function | Resource Utilization Min / Max |  | 
 | LUTs | Registers | BRAMs
Input arbiter | 2.1x / 3.4x | 1.8x / 2.8x | 0.9x / 1.3x
Output queue | 1.4x / 2.0x | 2.0x / 3.2x | 0.9x / 1.2x
Header parser | 0.9x / 3.2x | 2.1x / 3.2x | N/A
Openflow table | 0.9x / 1.6x | 1.6x / 2.3x | 1.1x / 1.2x
IP checksum | 4.3x / 12.1x | 9.7x / 32.5x | N/A
Encap | 0.9x / 5.2x | 1.1x / 10.3x | N/A
Notes: Finally, we study the area cost overhead of ClickNP compared to hand-written Verilog.
We pick up NetFPGA, which comes from Stanford and has good code quality.
For ClickNP, we implement equivalent functionality of several NetFPGA functions.
For most elements, overall the area cost overhead is less than two times.

## Slide 32: Area cost
Overhead compared to hand-written Verilog
NetFPFA Function | Resource Utilization Min / Max |  | 
 | LUTs | Registers | BRAMs
Input arbiter | 2.1x / 3.4x | 1.8x / 2.8x | 0.9x / 1.3x
Output queue | 1.4x / 2.0x | 2.0x / 3.2x | 0.9x / 1.2x
Header parser | 0.9x / 3.2x | 2.1x / 3.2x | N/A
Openflow table | 0.9x / 1.6x | 1.6x / 2.3x | 1.1x / 1.2x
IP checksum | 4.3x / 12.1x | 9.7x / 32.5x | N/A
Encap | 0.9x / 5.2x | 1.1x / 10.3x | N/A
Notes: For small elements, the overhead is relatively large, but the absolute overhead is small.
This is because every element is compiled to a logic block. High-level synthesis tools generate a wrapper with a fixed logic overhead.

## Slide 33: Area cost
Overhead compared to hand-written Verilog
NetFPFA Function | Resource Utilization Min / Max |  | 
 | LUTs | Registers | BRAMs
Input arbiter | 2.1x / 3.4x | 1.8x / 2.8x | 0.9x / 1.3x
Output queue | 1.4x / 2.0x | 2.0x / 3.2x | 0.9x / 1.2x
Header parser | 0.9x / 3.2x | 2.1x / 3.2x | N/A
Openflow table | 0.9x / 1.6x | 1.6x / 2.3x | 1.1x / 1.2x
IP checksum | 4.3x / 12.1x | 9.7x / 32.5x | N/A
Encap | 0.9x / 5.2x | 1.1x / 10.3x | N/A
Area cost will be less of a concern
Quickly growing FPGA capacity: 1x (2013), 2.5x (2015), 10x (2018)
Notes: Furthermore, the capacity of FPGA is growing quickly in recent years.
We believe that the area cost will be less of a concern in the future.

## Slide 34: Conclusion
FPGA in the cloud
  Fast, general and mature
ClickNP: programming hardware as software
  Highly flexible: Program with high-level language
  Modular: Click-like abstractions
  High performance: Utilize massive parallelism in FPGA
  Joint CPU/FPGA packet processing
Notes: Finally, the conclusion.
FPGA is fast, general and mature, so we have deployed FPGA at scale in the cloud.
This work presents ClickNP, a network processing platform to enable software developers to program hardware, which is highly flexible, modular, high performance and supports joint CPU/FPGA packet processing.
In addition to network processing, ClickNP is a general framework for programming on FPGA.
With FPGAs in datacenters, we can go beyond the memory wall and reach a fully programmable world.

## Slide 35: Development after the paper
Network → general stream processing
FPGA development platform for research and engineering projects in our research team
Applications:
Hardware-based Network Transport (Yuanwei Lu, APNet’17)
In-memory Key-value Store (Zhenyuan Ruan, SOSP’17)
HTTPS (RSA) Accelerator (Guo Chen and Tianyi Cui, MS Hackathon’16)
DeepCrossing DNN inference (Qiang Lou, Bing)
Regex Matching (Guo Chen, MS Techfest’17)
Multi-path RDMA (Yuanwei Lu)
Container Networking (Zibo Wang, MS Hackathon’17, SOSP’17 SRC)
Total-Order Multicast (Gefei Zuo, SOSP’17 SRC)
And more…
Extending ClickNP framework:
Distributed ClickNP (Guo Chen)
And more…
Notes: After the paper submission, the ClickNP project does not end.
ClickNP moves from network processing to general stream processing, and enables multiple research and engineering projects in our team, including applications. For example, Yuanwei’s paper on Memory Efficient Loss Recovery, which he will present this afternoon.
And extending the ClickNP framework to distribute to a cluster of FPGAs, and use Go language to support concurrency more naturally.

## Slide 36: 2.1. Virtual Storage Acceleration
Hypervisor
VM1
VM2
VM3
Compute Node
Programmable NIC
Network Node
Data Center Network
vNIC1
vNIC2
vNIC3
Virt Disk
Virt Net
Programmable
NIC
VNF Data Plane
VNF Control Plane
App
OS
App
OS
App
OS
Mem / Flash
Data Structure
NIC
Storage Node
DDR / Flash

## Slide 37: 2.2. Data Structure Acceleration
Hypervisor
VM1
VM2
VM3
Compute Node
Virt Disk
Virt Disk
Virt Net
NIC
Network Node
Storage Node
Data center network
App
OS
App
OS
App
OS
DDR / Flash
Programmable
NIC
VNF Data Plane
VNF Control Plane
DDR / Flash
Programmable
NIC
Data Structure Data Plane
Data Structure Control Plane

## Slide 38: KV-Direct: High-Performance In-Memory Key-Value Store with Programmable NIC
Bojie Li1,2 Zhenyuan Ruan1,3 Wencong Xiao1,4 Yuanwei Lu1,2 Yongqiang Xiong1 Andrew Putnam1 Enhong Chen2
Lintao Zhang1
1Microsoft Research 2USTC 3UCLA 4Beihang University
SOSP ’17
Notes: Thanks Adita for the introduction.
Hello everyone, I’m Bojie Li, a fourth year PhD student in a joint PhD program of USTC and Microsoft Research.
In this session we have seen two wonderful works, Eris and NetCache to use in-network processing with dataplane programmable switches to accelerate systems.
Now I will show programmable NICs can also be very useful in accelerating datacenter workloads.
Our KV-Direct work is done during internship in Microsoft Research Asia with my colleagues. Zhenyuan Ruan and me are co-first authors who design and implement this system together.

## Slide 39: Key-Value Store in Data Centers
Web Cache
Recent Tweets
User ID
SQL
Query result
Key
Value
Session
Browser cookies
Notes: As everyone knows, traditional key-value stores like memcached or redis are used for caching in web services.

## Slide 40: Key-Value Store in Data Centers
Web Cache
Shared Data Structure
Recent Tweets
User ID
SQL
Query result
Key
Value
Session
Browser cookies
Graph node
Feature
Weight
Key
Value
Shard
Sequence number
List of edges
More demanding workload
Notes: In recent years, key-value store goes beyond object caching and becomes an infrastructure service to store shared data structure in a distributed system.
Examples include parameter servers in machine learning, graph computing engine and sequencers for distributed transactions, as the Eris paper in this session just said.
Shared data structure stores demands more performance compared to web cache.

## Slide 41: Key-Value Store in Data Centers
Shared Data Structure
Graph node
Feature
Weight
Key
Value
Shard
Sequence number
List of edges
Design Goals
High throughput
Low tail latency
Write intensive
Vector operations ____
Atomic operations
More demanding workload
Notes: These shared data structure stores have enormous throughput requirement, for example a graph computation application may need billions of key-value operations per iteration.
Second, it requires low tail latency because the latency of an application is typically determined by the slowest one.
Third, the workload is no longer read intensive, so both reads and writes need to be efficient.
Finally, we should have built in support for vector operations and atomic operations.

## Slide 42: Key-Value Store Architectures
Software (Kernel TCP/IP)
Bottleneck: Network stack in OS (~300 Kops per core)
Notes: Key-value store is a holistic exercise of systems, including networking, computation and memory accesses.
For traditional key-value stores such as memcached and redis, the bottleneck is network stack in operating system. We all know that TCP/IP stack are slow.

## Slide 43: Key-Value Store Architectures
Software
e.g. DPDK, mtcp, libvma, two-sided RDMA
Bottlenecks: CPU random memory access and KV operation computation
(~5 Mops per core)
(Kernel Bypass)
Software (Kernel TCP/IP)
Bottleneck: Network stack in OS (~300 Kops per core)
Notes: Next, researchers use kernel-bypass networking to mitigate the network stack overhead.
One way is to build a lightweight network stack in user-mode.
Another way is to leverage two-sided RDMA to offload the networking stack into NIC hardware.
However, the throughput bottleneck is now CPU random access and key-value operation computation.

## Slide 44: Key-Value Store Architectures
Software (Kernel TCP/IP)
Bottleneck: Network stack in OS (~300 Kops per core)
One-sided RDMA
Communication overhead: multiple round- trips per KV operation (fetch index, data)
Synchronization overhead: write operations
Software
e.g. DPDK, mtcp, libvma, two-sided RDMA
Bottlenecks: CPU random memory access and KV operation computation
(~5 Mops per core)
(Kernel Bypass)
Notes: Another key-value store architecture is to bypass the server CPU entirely using one-sided RDMA.
The KV processing is offloaded to clients, and they access the key-value store via remote memory access.
However, in this design, there is significant communication overhead due to multiple round-trips per KV operation.
Furthermore, when clients need to write on a same key-value pair, they need synchronization to ensure consistency.

## Slide 45: Key-Value Store Architectures
Software (Kernel Bypass)
One-sided RDMA
KV-Direct FPGA + NIC
Offload KV processing on CPU to Programmable NIC
Software (Kernel TCP/IP)
Notes: We propose KV-Direct to offload KV processing on CPU to programmable NIC.
The name of KV-Direct means that the NIC directly fetches data and applies updates in the host memory to serve KV requests, completely bypassing server CPU.

## Slide 46: KV-Direct Architecture
NIC
Network Decoder
Request Scheduler
Hash Table
Network Encoder
Load Dispatch
PCIe (host mem)
On-board DRAM
Slab Allocator
Notes: Now we look at the architecture of KV-Direct.
key-value operations are received from the NIC and decoded in the network decoder,
Then the request scheduler issues independent key-value operations to the hash table,
Small key-value pairs are stored inline in the hash table, while larger key-value pairs are stored in dynamically allocated memory, which requires a slab memory allocator.
The memory accesses are dispatched to either on-board DRAM, or the PCIe bus to access host memory.
When the memory lookup result comes back, finally we encode the KV operation results and send to the client.

## Slide 47: Performance Challenges
ToR switch
Host DRAM (256 GB)
PCIe Gen3 x16 DMA
40 GbE
FPGA
CPU
NIC
Reconfigurable NIC
On-board DRAM (4 GB)
13 GB/s
120 Mops
Header overhead and limited parallelism: Be frugal on memory accesses
Notes: First, our PCIe interface between FPGA and host memory has limited throughput.
There is something worse. PCIe transport layer packets has header overhead, and the PCIe IP core in our FPGA has limited parallelism, which limits our PCIe throughput to 120 million operations per second.
So we need to be frugal on memory accesses.

## Slide 48: Performance Challenges
ToR switch
Host DRAM (256 GB)
PCIe Gen3 x16 DMA
40 GbE
FPGA
CPU
NIC
Reconfigurable NIC
On-board DRAM (4 GB)
1us delay
120 Mops
Atomic operations have dependency:
PCIe latency hiding
Notes: Second, the PCIe bus has delay of nearly 1 microsecond, due to additional delay in the PCIe IP core in our FPGA.
When atomic operations operate on the same key, they depend on the result of each other and needs to executed one by one.
Therefore, we need to hide the PCIe latency, otherwise the throughput will degrade to 1 million operations per second.

## Slide 49: Performance Challenges
ToR switch
Host DRAM (256 GB)
PCIe Gen3 x16 DMA
40 GbE
FPGA
CPU
NIC
Reconfigurable NIC
On-board DRAM (4 GB)
1us delay
120 Mops
0.2us delay
100 Mops
Load dispatch
Notes: Third, we hope to leverage both the throughput of on-board DRAM and host DRAM, so we need an efficient load dispatch mechanism.

## Slide 50: Performance Challenges
ToR switch
Host DRAM (256 GB)
PCIe Gen3 x16 DMA
40 GbE
FPGA
CPU
NIC
Reconfigurable NIC
On-board DRAM (4 GB)
1us delay
120 Mops
60 Mpps
Client-side batching
Vector-type operations
0.2us delay
100 Mops
Notes: Finally, because network packet headers also have significant overhead, we leverage client-side batching and support vector-type operations to reduce network overhead.

## Slide 51: Scalability with Multiple NICs
Notes: Because a single KV-Direct NIC has not saturated the bandwidth of host DRAM, we can leverage multiple programmable NICs to scale up the KV-Direct system. As we can see in the figure, the throughput increases almost linearly with number of NICs.

## Slide 52: Scalability with Multiple NICs
1.22 billion KV op/s
357 watts power
Notes: This photo is our test server with 10 programmable NICs, two Xeon E5 processors and 128 Gigabytes of memory.
Each programmable NIC is connected to the motherboard via 8 lanes of PCIe Gen3, so the 10 NICs saturate the 80 PCIe lanes from two Xeon E5 processors.
(click) With 10 programmable NICs, KV-Direct achieves 1.2 billion key-value operations per second with less than 400 watts of power consumption, setting a new milestone for general purpose key-value stores.

## Slide 53: KVS Performance Comparison
 | Tput (Mops) (GET / PUT) | Power (Kops/W) | Comment | Latency (us) (GET / PUT)
Memcached | 1.5 / 1.5 | 5 / 5 | TCP/IP | 50 / 50
MemC3 | 4.3 / 4.3 | 14 / 14 | TCP/IP | 50 / 50
RAMCloud | 6 / 1 | 20 / 3.3 | Kernel bypass | 5 / 14
MICA (12 NICs) | 137 / 135 | 342 / 337 | Kernel bypass | 81 / 81
FARM | 6 / 3 | 30 (261) / 15 | One-side RDMA | 4.5 / 10
DrTM-KV | 115 / 14 | 500 (3972) / 60 | One-side RDMA | 3.4 / 6.3
HERD | 35 / 25 | 490 / 300 | Two-side RDMA | 4 / 4
FPGA-Xilinx | 14 / 14 | 106 / 106 | FPGA | 3.5 / 4.5
Mega-KV | 166 / 80 | 330 / 160 | GPU | 280 / 280
KV-Direct (1 NIC) | 180 / 114 | 1487 (5454) / 942 (3454) | Programmable NIC | 4.3 / 5.4
KV-Direct (10 NICs) | 1220 / 610 | 3417 (4518) / 1708 (2259) | Programmable NIC | 4.3 / 5.4
* Number in parenthesis indicates power efficiency based on power consumption of NIC only, for server-bypass systems.
Notes: KV-Direct achieves high throughput and power efficiency compared to existing work.
In the table we show several existing systems, including traditional TCP IP, kernel-bypass networking, RDMA, FPGA and GPU.

## Slide 54: KVS Performance Comparison
 | Tput (Mops) (GET / PUT) | Power (Kops/W) | Comment | Latency (us) (GET / PUT)
Memcached | 1.5 / 1.5 | 5 / 5 | TCP/IP | 50 / 50
MemC3 | 4.3 / 4.3 | 14 / 14 | TCP/IP | 50 / 50
RAMCloud | 6 / 1 | 20 / 3.3 | Kernel bypass | 5 / 14
MICA (12 NICs) | 137 / 135 | 342 / 337 | Kernel bypass | 81 / 81
FARM | 6 / 3 | 30 (261) / 15 | One-side RDMA | 4.5 / 10
DrTM-KV | 115 / 14 | 500 (3972) / 60 | One-side RDMA | 3.4 / 6.3
HERD | 35 / 25 | 490 / 300 | Two-side RDMA | 4 / 4
FPGA-Xilinx | 14 / 14 | 106 / 106 | FPGA | 3.5 / 4.5
Mega-KV | 166 / 80 | 330 / 160 | GPU | 280 / 280
KV-Direct (1 NIC) | 180 / 114 | 1487 (5454) / 942 (3454) | Programmable NIC | 4.3 / 5.4
KV-Direct (10 NICs) | 1220 / 610 | 3417 (4518) / 1708 (2259) | Programmable NIC | 4.3 / 5.4
* Number in parenthesis indicates power efficiency based on power consumption of NIC only, for server-bypass systems.
Notes: The throughput of KV-Direct is equivalent to 20 to 30 CPU cores.
The MICA system uses 12 NICs, but we achieve the throughput with only a single NIC.
Although the GET throughput of DrTM is high, the PUT throughput is low, this is because it uses one-sided RDMA and the clients need synchronization to keep consistency on write operations.
The Mega-KV system uses GPU, although the throughput of GPU memory is high, its capacity is much smaller than the host memory.

## Slide 55: KVS Performance Comparison
 | Tput (Mops) (GET / PUT) | Power (Kops/W) | Comment | Latency (us) (GET / PUT)
Memcached | 1.5 / 1.5 | 5 / 5 | TCP/IP | 50 / 50
MemC3 | 4.3 / 4.3 | 14 / 14 | TCP/IP | 50 / 50
RAMCloud | 6 / 1 | 20 / 3.3 | Kernel bypass | 5 / 14
MICA (12 NICs) | 137 / 135 | 342 / 337 | Kernel bypass | 81 / 81
FARM | 6 / 3 | 30 (261) / 15 | One-side RDMA | 4.5 / 10
DrTM-KV | 115 / 14 | 500 (3972) / 60 | One-side RDMA | 3.4 / 6.3
HERD | 35 / 25 | 490 / 300 | Two-side RDMA | 4 / 4
FPGA-Xilinx | 14 / 14 | 106 / 106 | FPGA | 3.5 / 4.5
Mega-KV | 166 / 80 | 330 / 160 | GPU | 280 / 280
KV-Direct (1 NIC) | 180 / 114 | 1487 (5454) / 942 (3454) | Programmable NIC | 4.3 / 5.4
KV-Direct (10 NICs) | 1220 / 610 | 3417 (4518) / 1708 (2259) | Programmable NIC | 4.3 / 5.4
* Number in parenthesis indicates power efficiency based on power consumption of NIC only, for server-bypass systems.
Notes: On the power efficiency part, KV-Direct is 10x power efficient than existing work with pure CPU, one-sided RDMA, two-sided RDMA or GPU. Number in parenthesis indicates power efficiency based on power consumption of NIC only, for server-bypass systems. This methodology is justified because other workload can still run on CPU with little performance impact.
(click) Finally, the latency of KV-Direct is on-par with the best of other systems.

## Slide 56: Conclusion
Leverage the SmartNIC to access remote data structures in host memory without involving CPU
Key-value store is only an example
QPI
DRAM
DRAM
NIC
CPU
1
QSFP
40Gb/s
2
ToR
Gen3 x8
Gen3 2x8
FPGA
DRAM
CPU
40Gb/s
QSFP
QSFP

## Slide 57: 3. Acceleration of OS Communication Primitives
Hypervisor
VM1
VM2
VM3
Compute Node
Programmable
NIC
Data Center Network
vNIC1
vNIC2
vNIC3
Virt Disk
Virt Net
App
OS (Socket)
App
App
Mem / Flash
Communication Protocol
Network Node
Storage Node
Programmable
NIC
VNF Data Plane
VNF Control Plane
DDR / Flash
Programmable
NIC
Data Structure Data Plane
Data Structure Control Plane
OS (Socket)
OS (Socket)

## Slide 58: SocksDirect: Datacenter Sockets can be Fast and Compatible
Bojie Li*1,2 Tianyi Cui*3 Zibo Wang1,2 Wei Bai1 Lintao Zhang1
1Microsoft Research 2USTC 3University of Washington
* Co-first authors
SIGCOMM ‘19

## Slide 59: The Socket Communication Primitive
socket()
bind()
listen()
accept()
recv()
send()
close()
Server
Client
socket()
connect()
send()
recv()
close()
Notes: As we all know, most applications use the socket primitive for inter-process communication, both within a same server and among different servers.

## Slide 60: Socket: a Performance Bottleneck
Socket syscall time >> user application time
Chart: 
| Lighttpd HTTP Server | Nginx HTTP Load Balancer | Redis Key-Value Store | NSC DNS Server
Kernel time | 0.78 | 0.77 | 0.87 | 0.92
User application time | 0.22 | 0.23 | 0.13 | 0.08
Socket latency >> hardware transport latency
Chart: 
| Intra-host (vs. shared memory) | Inter-host (vs. RDMA)
shared memory (SHM) / RDMA | 0.25 | 1.6
Linux Socket | 11 | 30
Notes: Traditionally, sockets are implemented in the OS kernel. We all know that kernel socket is very slow. To show this point, we profile several popular applications in data centers. We can see that 70% to 90% of CPU time is used in OS kernel, which means it is handling the socket system calls. If we could eliminate the overhead of OS kernel and all CPU time can be utilized by the user space application, the application throughput will improve by several times.
Next we look at the latency, and the problem is more severe than throughput. For communication between two directly connected servers, socket latency is 17x of RDMA. For intra-host communication, socket latency is 40x of shared memory queue. In this work, we try to answer one question: is this socket overhead an intrinsic property of the socket abstraction, or we can do something to eliminate the socket overhead?

## Slide 61: High Performance Socket Systems
User App
User App
User App
Kernel VFS
Host 1
Host 2
Kernel Optimization
FastSocket, Megapipe, StackMap…
User-space TCP/IP
Offload to RDMA NIC
IX, Arrakis, SandStorm, mTCP, LibVMA, OpenOnload…
Rsocket, SDP, FreeFlow…
User App
User-space VFS
User App
User-space VFS
Host 1
TCP/IP
TCP/IP
User App
Host 2
Kernel TCP/IP
NIC packet API
User-space TCP/IP
User-space TCP/IP
NIC packet API
NIC packet API
Kernel
NIC packet API
User-space Stack
User App
User-space VFS
User App
User-space VFS
Host 1
RDMA
User App
Host 2
NIC RDMA API Hardware-based Transport
NIC RDMA API
User-space VFS
Notes: There have been extensive research to improve the performance of socket systems.
The first category is to optimize the kernel. A socket stack basically divides into three layers. The first layer is the virtual file system, VFS, because each socket connection is regarded as a file in Linux, and a file descriptor is mapped for the socket. The second layer is the kernel TCP/IP stack that provides the transport function. The third layer is the hardware interface layer. Linux kernel uses a packet API.
The second category is to implement the VFS abstraction and TCP/IP transport in the user space. It not only move the kernel functions into user space, but also greatly simplify the functions, for example, use polling to avoid the interrupt and process scheduling overheads.
The third category is to offload the transport to the NIC. Here we recall some history of hardware-based transports. TCP offload is not a new thing. In 1990s, there has been Ethernet cards that

## Slide 62: SocksDirect Design Goals
Compatibility
Drop-in replacement, no application modification
Isolation
Security isolation among containers and applications
Enforce access control policies
High Performance
High throughput
Low latency
Scalable with number of CPU cores

## Slide 63: SocksDirect: Fast and Compatible Socket in User Space
Process 1
Process 2
Event queue
Request queue
Application
User Mode
Kernel Mode
Shared Buffer
Event queue
Request queue
Application
Data
Data
Monitor Process
Monitor: user-space daemon process to coordinate global resources and enforce ACL rules.
Processes as a shared-nothing distributed system: use message passing over shared-memory queues.
ACL rules
connect
send
recv
accept

## Slide 64: SocksDirect Supports Different Transports for Data
User App
libsd
User App
libsd
User App
libsd
User App
TCP/IP
TCP/IP
Monitor
Host 1
Host 2
Host 3
No SocksDirect
Monitor
Mem Queue
Mem Queue
Mem Queue
TCP/IP
RDMA
NIC RDMA API
NIC Packet API
NIC RDMA API

## Slide 65: Microbenchmarks
Latency
Throughput
Notes: Intra-host: 8B latency close to shared memory queue, 4x lower than Rsocket and LibVMA because they use NIC to forward intra-host packets. 35x lower than Linux.
Inter-host: 8B latency even lower than two-sided RDMA send and receive, because we use one-sided RDMA write. Half of Rsocket, performance gain due to buffer management. 7x lower than LibVMA because it needs batching. Latency 17x lower than Linux.

## Slide 66: Application Performance
Nginx HTTP server request latency
Notes: Nginx HTTP server between two hosts: small HTTP messages, 5x lower than Linux. For large message, 13x lower than Linux due to zero copy.

## Slide 67: Cloud Acceleration based on Programmable NIC
Hypervisor
VM1
VM2
VM3
Compute Node
Programmable
NIC
Data Center Network
vNIC1
vNIC2
vNIC3
Virt Disk
Virt Net
App
OS (Socket)
App
App
Mem / Flash
Communication Protocol
Network Node
Storage Node
Programmable
NIC
VNF Data Plane
VNF Control Plane
DDR / Flash
Programmable
NIC
Data Structure Data Plane
Data Structure Control Plane
OS (Socket)
OS (Socket)

## Slide 68
NSDI ‘19

## Slide 69: Current FPGA communication architecture

## Slide 70: Current FPGA communication architecture

## Slide 71: Problem #1: Programming Interface

## Slide 72: Problem #2: Accessibility

## Slide 73: Problem #3: Multiplexing

## Slide 74: Problem #3: Multiplexing

## Slide 75: Problem #4: Security

## Slide 76: Problem #4: Security

## Slide 77: Direct Universal Access

## Slide 78: Direct Universal Access

## Slide 80: Evaluation: Logic Overhead

## Slide 81: Outline
Why SmartNICs
SmartNIC applications
  ClickNP: highly flexible and high performance network processing with FPGA
  KV-Direct: a high-performance in-memory key-value store with FPGA
  SocksDirect: high performance socket communication
  DUA: making data center resources available to FPGA
The future of SmartNIC architecture

## Slide 82: Tight Integration with host CPU
Core 1
Core 2
Core 3
NIC
Mem controller
DDR
PCIe RC
PCIe
Core 1
Core 2
Core 3
NIC
Mem controller
DDR
Recall: In KV-Direct, when accessing data structures in host memory, why do we need to be frugal on memory accesses? Why do we need to hide the PCIe latency?
SoC

## Slide 83: Disaggregated Pool of Tiered Memory
Towards memory disaggregation in a cluster
  Motivation 1: 40% hardware cost of cloud servers is DDR. VM memory usage is highly unbalanced, and 40% provisioned memory capacity is unused. Borrowing memory from other nodes in the cluster can expand memory capacity.
  Motivation 2: Big data and database applications require PB-scale storage, which needs to store large data structures in a cluster.
Towards disaggregated pool of tiered memory
  DDR/Optane/Flash are different classes of storage with different capacity, price, and persistence.
  DDR should be a performance layer holding the hot data.

## Slide 84: Disaggregated Pool of Tiered Memory
Problem: latency of remote memory and Flash storage is much higher than local DDR access!
CPU
DDR
Flash
Host 1
CPU
DDR
Flash
Host 2
CPU
DDR
Flash
Host 3
Network RTT = 3 us
Flash latency = 30 us
DDR latency = 0.1 us

## Slide 85: Heterogenous Data Access Methods
Compute at Client
Memory-mapped Load/Store
(CXL, Gen-Z, etc.)
Asynchronous Read/Write
(one-sided RDMA)
Compute at Server
(Home Node of Data)
SmartNIC Offloading
In-Network Computation
RPC on CPU
Load/Store: low overhead per operation, but synchronous; may have cache and buffer
Read/Write: high overhead per operation, but each op can transfer a large block, and many ops can work in parallel
Switch: high throughput but low programmability and buffer size
SmartNIC: high parallelism but high PCIe latency and low buffer size
RPC on CPU: close to memory, easy to program but high cost
How to choose among the data access methods?
Can we have a unified programming framework?
Notes: Now we have heterogenous methods to access a piece of remote data in data center networks. Traditionally, the only way to access remote data is by executing RPC on the remote CPU. Then we have RDMA technology to directly copy the data to local buffer and do computation. If the data structure is complicated, we may need multiple network round-trips to RDMA the data. But because it removes the cost to invoke an RPC on the remote CPU, which is mainly the TCP/IP and RPC protocol stack, the overall performance may be still higher. Next we have smartNIC offloading and in-network computation. SmartNIC is high parallelism but its main drawback is high PCIe latency and low on-chip buffer size. Network switches also have low buffer size but high throughput. In the next a few years we will have memory-mapped load/store over network, which has lower per-operation overhead compared to reads and writes, but each operation only accesses a cache line of data. In summary, we have a wide spectrum of data access methods, and we need some way to choose among them.

## Slide 86: RPC at Server CPU
DPDK, ZygOS, Shinjuku, Shenango, eRPC…
Source: Datacenter RPCs can be General and Fast, NSDI’19

## Slide 87: Hardware-accelerated RPC at Server
RPCvalet, NeBuLa (Scale-Out NUMA), NanoPU…
Source: The nanoPU: A Nanosecond Network Stack for Datacenters, OSDI’21

## Slide 88: Hardware-accelerated RPC at Server
Source: The nanoPU: A Nanosecond Network Stack for Datacenters, OSDI’21
RPCvalet, NeBuLa (Scale-Out NUMA), NanoPU…

## Slide 89: SmartNIC Offloading at Server
Actor Programming Model
  Each actor has local state and communicates with explicit messages
Source: Offloading Distributed Applications onto SmartNICs using iPipe, SIGCOMM’19
ClickNP
iPipe
RMT: Reconfigurable Match-action Table

## Slide 90: SmartNIC Offloading at Client
Traditional CPU cores have limited capability of hiding memory latency, especially when accessing remote memory and Flash storage with 3us+ latency. The CPU core is stuck waiting without scheduling other tasks.
The solution: hardware multithreading.
Adding hardware multithreading to the main CPU is too complicated, so we consider building such a co-processor in SmartNICs.
The host CPU should offload tasks with a lot of remote memory accesses which cannot be simply offloaded to the remote side.
The co-processor should have multiple hardware threads to hide load/store latency. When a hardware thread executes a slow load (remote or slow storage media), the thread should be paused and the hardware scheduler finds another ready thread to execute.

## Slide 91: Improving Data Locality
In a disaggregated pool of tiered memory:
  When using remote memory to expand local memory, hot data should be in local memory.
  Hot data in the cluster should be in DDR rather than slow storage media.
Open question: how to do data hotness measurement and migration?
Can we cache hot data at clients?
  How to maintain cache coherence among clients and server?

## Slide 92: Conclusion
Infrastructure services in data centers mainly use software processing on general processors, whose performance lags behind networking, storage and customized computing hardware.
To provide high performance and flexibility, recent years witnessed large scale deployment of programmable NICs (SmartNICs) in data centers.
We use SmartNICs to offload network functions, remote data structures, and OS communication primitives.
Future SmartNICs will be tightly integrated with host CPU, support programmable offloading, and build the data plane for disaggregated pool of tiered memory.

## Slide 93: Thanks!
Q&A