## Slide 1: Network Intelligence: NIC, switch or xPU?
Bojie Li
Co-Founder, Logenic AI
Sep 16, 2023

## Slide 2: Contents
Trend 1: Intelligent Network Devices
  SmartNIC: FPGA, ASIC, NP and DPU
  Programmable Switch
Trend 2: Fast Interconnect
  NVLink and CXL: Direct P2P with Memory Semantics
  Convergence of AI and Cloud Networking

## Slide 3: Trend 1: Intelligent Network Devices
SmartNICs
(Microsoft)
Programmable Switches
(Barefoot Tofino)

## Slide 4: Types of SmartNICs
FPGA/ASIC On-Path SmartNICs
(Microsoft Catapult)
NP-based On-Path SmartNICs (Huawei Hi1822)
Off-Path SmartNICs (DPU)
(Mellanox BlueField)
Host CPU
FPGA
RDMA NIC
ToR Switch
PCIe
Ethernet
Ethernet
PCIe
Host CPU
Hi1822 NIC
MIPS Cores
Hardware Engine
Host CPU
BlueField NIC
ARM Cores
PCIe Switch
RDMA NIC
ToR Switch
ToR Switch

## Slide 5: FPGA-based On-Path SmartNICs
A Cloud-Scale Acceleration Architecture, ISCA ’16 (Microsoft)
Since 2016, every new server in Azure has deployed an FPGA-based SmartNIC
Network virtualization
Storage virtualization
Bing ranking acceleration
Compression acceleration
Encryption acceleration

## Slide 6: SmartNICs in the Public Cloud
Network Virtualization consumes CPUs, e.g., 5 physical cores per host.
Each physical core sells for $0.1 per hour.
  Max potential value $900 per year.
  $4500 over the lifetime of a server.
How much does an FPGA-based SmartNIC cost?
  Less than $1000 when purchased in large bulk.
Azure Accelerated Networking: SmartNICs in the Public Cloud, NSDI ’18 (Microsoft)

## Slide 7: SmartNICs in the Public Cloud
Azure Accelerated Networking: SmartNICs in the Public Cloud, NSDI ’18 (Microsoft)

## Slide 8: Challenges of FPGA-based SmartNICs

## Slide 9: FPGA Programming Made Simple
ClickNP: Highly Flexible and High Performance Network Processing with Reconfigurable Hardware, SIGCOMM ‘16

## Slide 10: When to Use FPGA – the 10/100/1000 Rule
10 – 10 years of workload lifetime
  If the workload is shifting too fast, FPGA is not as agile as CPUs
100 – 100 lines of C++ code
  If the workload is too complicated, an FPGA implementation consumes too much area
1000 – 1000 servers
  If the workload is too lightweight, the FPGA development cost is hard to amortize

## Slide 11: ASIC-based On-Path SmartNICs: AWS Nitro
Traditional: Hypervisor (dom0) consumes several cores
  Network virtualization (VPC)
  Storage virtualization
    Local instance storage
    Network-attached EBS volumes
  Management
Security benefits of the Nitro architecture - SEP401-R - AWS re:Inforce 2019

## Slide 12: AWS Nitro Removes Hypervisor CPU Cost
Security benefits of the Nitro architecture - SEP401-R - AWS re:Inforce 2019

## Slide 13: AWS Nitro Enables Bare-Metal Instance
Security benefits of the Nitro architecture - SEP401-R - AWS re:Inforce 2019

## Slide 14: AWS Nitro Provides Security Benefits
Security benefits of the Nitro architecture - SEP401-R - AWS re:Inforce 2019

## Slide 15: AWS Nitro Provides Security Benefits
Security benefits of the Nitro architecture - SEP401-R - AWS re:Inforce 2019

## Slide 16: AWS Nitro Provides Security Benefits
Security benefits of the Nitro architecture - SEP401-R - AWS re:Inforce 2019

## Slide 17: NP-based On-Path SmartNICs
Huawei Hi1822 SmartNIC
Transaction State
DMA Input
Request Scheduler
Network Input
Connection State Store
DMA Output
Data and command from CPU
Flow Processing Cores
Request data and transaction state
Request complete or wait for DMA/next packet;
Update transaction state
Request Data
Response Data
Send data to CPU
Hardware Accelerators
Output Queue
Egress Packets
On-chip Network
Packet Processing Cores (Match-Action Table)
Network Output
Packet Processing Cores (Match-Action Table)
Ingress Packets
Cavium OCTEON II 68xx
Netronome Agilio CX SmartNIC

## Slide 18: NP-based SmartNICs: Hard to Program
Need to read 1000+ pages of documents
  10+ data structure and 10+ packet processing accelerators on chip
An NP-based RDMA implementation has 10K+ lines of C code
  Limited instruction cache: cache thrashing if not optimized
  Need to carefully arrange the hot paths to make sure it fits in the cache
Need to pipeline accesses to DMA and data structures on chip
  A classical latency hiding problem: the trade-off between polling and context switch
  When the flow processing cores waits for data structure access and locks, if it switches context to other QP contexts, loading the context takes time
  Typical latencies: on-chip data structure access < context switch < DMA

## Slide 19: SoC-based Off-Path SmartNICs (aka. DPU)
Multi-core General Processors
RDMA NIC (Connect-X)
PCIe Switch
Data Center Network
NIC DRAM
Host DRAM
Host CPU
SmartNIC
Mellanox BlueField

## Slide 20: Off-Path vs. NP-based On-Path SmartNICs

## Slide 21: DPU is Not Yet Another CPU
NVIDIA DATA CENTER PROCESSING UNIT (DPU) ARCHITECTURE, HotChips 2021

## Slide 22: DPU Must Include Hardware Acceleration
NVIDIA DATA CENTER PROCESSING UNIT (DPU) ARCHITECTURE, HotChips 2021
DPU: A convergence of Off-Path and NP-based On-Path SmartNICs

## Slide 23: How to Choose SmartNICs?
ASIC and FPGA are similar.
  FPGA is more programmable.
  ASIC is cheaper in extremely large scale (1M+ hosts).
  Suitable for large cloud providers.
NP-based SmartNICs and DPUs are similar.
  Only offloading tasks to generic processors does not work.
  Hardware acceleration adds complexity to programming, but essential for performance.
  Suitable for small-to-medium scale deployments.

## Slide 24: Contents
Trend 1: Intelligent Network Devices
  SmartNIC: FPGA, ASIC, NP and DPU
  Programmable Switch
Trend 2: Fast Interconnect
  NVLink and CXL: Direct P2P with Memory Semantics
  Convergence of AI and Cloud Networking

## Slide 25: Programmable Switch: P4
 | Server | Switch
Example | [NetBricks, OSDI ’16] | Barefoot Tofino
Packets per second | ~30 million | > 1 billion
Bandwidth | 10-100 Gbps | 6.5 Tbps
Processing delay | 10-100 us | < 1 us
Visibility | Narrow | Wide
Memory capacity | Large | Small
Programmability | High | Low

## Slide 26: Use Case 1: NIC + Switch Congestion Control
HPCC: High Precision Congestion Control, SIGCOMM ‘19
Towards Compute-Native Networking, APNet ‘21

## Slide 27: Use Case 2: Sub-RTT Coordination on Switches
High throughput
Low latency
Strong consistency
Fault tolerance
Directly from high-performance switches
Chain replication in the network
NetChain: Scale-Free Sub-RTT Coordination, NSDI ‘18

## Slide 28: Use Case 3: SHARP for AI Param Aggregation
THE NVLINK-NETWORK SWITCH: NVIDIA’S SWITCH CHIP FOR HIGH COMMUNICATION-BANDWIDTH SUPERPODS, HotChips ‘22

## Slide 29: Why Intel Stopped Tofino

## Slide 30: SmartNIC or Programmable Switch?
Programmable Switch
Host
SmartNIC
CPU
Mem
Host
SmartNIC
CPU
Mem
 | SmartNIC | Programmable Switch
Congestion control | DCQCN, TIMELY, MP-RDMA, IRN | HPCC, pFabric, DeTail, CP, NDP
Load balancer | VFP | SilkRoad
Key-value store | Pilaf, FaRM, DrTM, FaSST, KV-Direct | SwitchKV, NetCache, IncBricks
Aggregation | NetAgg, CamCube | SHARP, DAIET, SwitchML, ATP
Lock | DSLR | NetLock
Coordination / Replication | Consensus in a Box, DARE, APUS, Derecho, Mu | NetChain, NetPaxos, SpecPaxos, NOPaxos, Eris
Programming system | Floem, iPipe, StRoM, ClickNP, FairNIC, λ-NIC | SNAP, Frenetic, P4, P4visor, 𝜇P4, Domino, Lyra, Gallium

## Slide 31: Contents
Trend 1: Intelligent Network Devices
  SmartNIC: FPGA, ASIC, NP and DPU
  Programmable Switch
Trend 2: Fast Interconnect
  NVLink and CXL: Direct P2P with Memory Semantics
  Convergence of AI and Cloud Networking

## Slide 32: Trend 2: Fast Interconnect
THE NVLINK-NETWORK SWITCH: NVIDIA’S SWITCH CHIP FOR HIGH COMMUNICATION-BANDWIDTH SUPERPODS, HotChips ‘22

## Slide 33: Why LLM Training Needs High Bandwidth

## Slide 34: Tensor Parallelism Needs High Bandwidth
Back-of-envelope estimation for tensor parallelism in attention computation (QKV), excluding FFNN:
Computation cost is roughly: 3 * batch size * token length * (embedding size * embedding size / num GPUs) * 2 flops
Communication cost is roughly: Batch size * token length * embedding size * 2 bytes
Computation / Communication = 3 * embedding size / num GPUs
Example: LLaMA-2 70B, embedding size = 8192
Computation FLOPS of H100: 989T Tensor flops for 16 bit
If we use 8 GPUs for tensor parallelism and assume 100% FLOPS utilization:
  Bandwidth >= Computation / (3 * embedding size / num GPUs) = 989T / (3 * 8192 / 8) = 321 GB/s
  Bi-direction bandwidth >= 642 GB/s
That’s why we need 900 GB/s bandwidth for NVLink

## Slide 35: Low Latency Is Not A Strict Requirement
Taking latency into account:
Communication time is roughly: (Batch size * token length * embedding size * 2 bytes / bandwidth) + latency
Computation time is roughly: 3 * batch size * token length * (embedding size * embedding size / num GPUs) * 2 flops / computation flops
Example: LLaMA-2 70B, embedding size = 8192, token length = 4096, batch size = 1
Communication time (NVLink) = (1 * 4096 * 8192 * 2 / 450G) + latency = 149 us + latency
Computation time = 3 * 1 * 4096 * (8192 * 8192 / 8) * 2 / 989T = 208 us
To achieve 100% FLOPS utilization: Latency <= 208 us – 149 us = 59 us
In datacenters NVLink/RDMA latency is typically <10 us, so latency is not a big problem for training.
However, latency predictability is important because congestion/PFC storm may bring >1ms high latency.

## Slide 36: Direct Peer-to-Peer Interconnect

## Slide 37: Convergence of Intra- and Inter-host Network
Network Switch
NIC
NIC

## Slide 38: Memory Semantics
Program
Mem
Mem
Program
Network
Message
Semantics
Example
ZeroMQ / Kafka
RDMA send/recv
Remote Memory Access
RDMA read/write /atomic
CXL Load/Store
RPC
gRPC, Thrift
Byte Stream
Socket send/recv
010101010
010
101
010
W 0xA: 010
W 0xB: 101
R 0xC
Invoke A(010)
Invoke A(101)
Invoke B(010)
Memory Semantics

## Slide 39: Exploiting Parallelism with Memory Semantics
RDMA is strictly in-order communication
  Hard to utilize multiple network paths due to reordering cost at receiver
  One lost packet blocks subsequent transactions from delivery
  Hard to support page faults because a slow page-fault memory access would block all subsequent accesses
Many memory accesses can be executed out-of-order
  Example: transferring multiple large tensors
  Parallelize transfer over multiple network paths to improve bandwidth
  A lost packet only blocks one transaction
  Page-fault and other slow memory accesses can be processed out-of-order

## Slide 40: Load/Store vs. Read/Write
Read/Write is asynchronous remote memory access
Requires multiple PCIe RTTs, min latency 1.6 us
App
WQE
NIC
doorbell
NIC
Mem
CQE
PCIe
PCIe
Load/Store is synchronous remote memory access. CPU accesses network directly.
No PCIe, No WQE, CQE or doorbell, latency < 0.5 us
App
I/O die
I/O die
Mem
①
②
③
④
⑤
Data
⑥
⑦
⑧
⑨
①
②
③
④

## Slide 41: Load/Store is Not a Panacea
 | Load/Store | Read/Write
Programming | Sync | Async
Granularity | Cache line | User-specified message size
Latency | Low | High
Access efficiency of large data blocks | Low | High
Application transparency | Application imperceptible, can be used to extend local memory, achieving memory pooling | The application needs explicit access to remote memory; if used for memory expansion, the application needs to be modified
Hardware requirements | High, requires the NIC to work closely with the CPU | Low, the NIC can be in a detached form
Reliability | Large blast radius, a node failure will affect all nodes using the remote memory of that node; store instruction fault is difficult to capture | Easy to capture asynchronous remote access exceptions through the application, reducing the blast radius to the affected application
Cache coherence | Depends on whether the hardware supports it, but the overhead of hardware supporting cache coherence is high at a large scale | Not supported, the software explicitly copies between remote and local memory. In the case of sharing, it needs to coordinate with distributed locks to ensure consistency

## Slide 42: GPU Comm.: From Load/Store to Read/Write
ARK: GPU-driven Code Execution for Distributed Deep Learning, NSDI ‘23

## Slide 43: Which Semantics to Pick?
Compute at Client
Memory-mapped Load/Store
(CXL, Gen-Z, etc.)
Asynchronous Read/Write
(one-sided RDMA)
Compute at Server
(Home Node of Data)
SmartNIC Offloading
In-Network Computation
RPC on CPU
Load/Store: low overhead per operation, but synchronous; may have cache and buffer
Read/Write: high overhead per operation, but each op can transfer a large block, and many ops can work in parallel
Switch (in-network): high throughput but low programmability and buffer size
SmartNIC: high parallelism but high PCIe latency and low buffer size
RPC on CPU: close to memory, easy to program but high cost

## Slide 44: Contents
Trend 1: Intelligent Network Devices
  SmartNIC: FPGA, ASIC, NP and DPU
  Programmable Switch
Trend 2: Fast Interconnect
  NVLink and CXL: Direct P2P with Memory Semantics
  Convergence of AI and Cloud Networking

## Slide 45: Convergence of AI and Cloud Networking
AI Network
Cloud Network

## Slide 46: Convergence of AI and Cloud Networking
NVIDIA DATA CENTER PROCESSING UNIT (DPU) ARCHITECTURE, HotChips 2021

## Slide 47: Region-scale RDMA for Disaggregated Storage
70% of Azure traffic is RDMA for disaggregated storage
Empowering Azure Storage with RDMA, NSDI ‘23

## Slide 48: Region-scale RDMA for Disaggregated Storage
Empowering Azure Storage with RDMA, NSDI ‘23
RDMA reduces CPU utilization
RDMA reduces storage latency
RDMA Benefits

## Slide 49: Region-scale RDMA for Disaggregated Storage
Challenges:
  PFC Storm caused by malfunctioning NICs and switches
  Interoperability of heterogenous NICs and switches
  Scaling PFC and congestion control over long-haul (~100 km) links between AZs
Empowering Azure Storage with RDMA, NSDI ‘23
Solutions:
  PFC Watchdog on switches and SmartNICs to distinguish PFC Storm from congestion PFCs
    Minimize PFC generation using per-flow E2E congestion control, BUT keep PFC to allow fast start and lower tail latency
  Fine-tune DCQCN for NIC inter-op; Switch – SONiC: unified software stack
  Jointly tune DCQCN params with switch buffers; sparse ECN marking; DCQCN does not suffer from RTT unfairness

## Slide 50: RDMA: The Devil is in the Details
Lumina: Understanding the Micro-Behaviors of Hardware Offloaded Network Stacks, SIGCOMM ‘23

## Slide 51: Performance Isolation Problem of RDMA NICs
Husky: Understanding RDMA Microarchitecture Resources for Performance Isolation, NSDI ‘23

## Slide 52: Lessons from Azure RDMA Deployment
Empowering Azure Storage with RDMA, NSDI ‘23

## Slide 53: The Congestion Challenge
Domain-Specific Interconnection Networks in the Era of Domain-Specific AI Supercomputer, APNet ‘23 Keynote

## Slide 54: Predictable RDMA Network for AI/HPC
1. Congestion Control
(DCQCN)
2. End-to-end Flow Control
(1RMA)
3. Flow Scheduling
(PIAS)
4. Traffic Engineering
(B4 in WAN, ? in datacenters)

## Slide 55: Predictable RDMA Network for AI/HPC
Domain-Specific Interconnection Networks in the Era of Domain-Specific AI Supercomputer, APNet ‘23 Keynote

## Slide 56: General-Purpose vs. Domain-Specific
Domain-Specific Interconnection Networks in the Era of Domain-Specific AI Supercomputer, APNet ‘23 Keynote

## Slide 57: My View on the Debate
Programmability and scalability first
  Programmability promotes ecosystem
  Scalability enables a unified architecture for many scenarios
  Identify bottlenecks in real systems before optimizing performance
Consider GPUs vs. DSAs
  DSAs have higher performance but CUDA has the best ecosystem
  The price of H100 ($30K~$40K) is 15~20x of its manufacturing cost ($2K)

## Slide 58: Summary
Trend 1: Intelligent Network Devices
  SmartNIC: FPGA, ASIC, NP and DPU
  Programmable Switch
Trend 2: Fast Interconnect
  NVLink and CXL: Direct P2P with Memory Semantics
  Convergence of AI and Cloud Networking
Where should we put network intelligence?
  The AI era is coming, so everything is going to be smart
  SmartNICs for virtualization, switches for In-Network Telemetry, direct P2P among xPUs with memory semantics
  Programmability and scalability first

## Slide 59: Thanks!