## Slide 1: SocksDirect: Datacenter Sockets can be Fast and Compatible
Bojie Li*1,2 Tianyi Cui*3 Zibo Wang1,2 Wei Bai1 Lintao Zhang1
1Microsoft Research 2USTC 3University of Washington
* Co-first authors

## Slide 2: The Socket Communication Primitive
socket()
bind()
listen()
accept()
recv()
send()
close()
Server
Client
socket()
connect()
send()
recv()
close()
Notes: As we all know, most applications use the socket primitive for inter-process communication, both within a same server and among different servers.

## Slide 3: Socket: a Performance Bottleneck
Socket syscall time >> user application time
Chart: 
| Lighttpd HTTP Server | Nginx HTTP Load Balancer | Redis Key-Value Store | NSC DNS Server
Kernel time | 0.78 | 0.77 | 0.87 | 0.92
User application time | 0.22 | 0.23 | 0.13 | 0.08
Socket latency >> hardware transport latency
Chart: 
| Intra-host (vs. shared memory) | Inter-host (vs. RDMA)
shared memory (SHM) / RDMA | 0.25 | 1.6
Linux Socket | 11 | 30
Notes: Traditionally, sockets are implemented in the OS kernel. We all know that kernel socket is very slow. To show this point, we profile several popular applications in data centers. We can see that 70% to 90% of CPU time is used in OS kernel, which means it is handling the socket system calls. If we could eliminate the overhead of OS kernel and all CPU time can be utilized by the user space application, the application throughput will improve by several times.
Next we look at the latency, and the problem is more severe than throughput. For communication between two directly connected servers, socket latency is 17x of RDMA. For intra-host communication, socket latency is 40x of shared memory queue. In this work, we try to answer one question: is this socket overhead an intrinsic property of the socket abstraction, or we can do something to eliminate the socket overhead?

## Slide 4: High Performance Socket Systems
User App
User App
User App
Kernel VFS
Host 1
Host 2
Kernel Optimization
FastSocket, Megapipe, StackMap…
User-space TCP/IP
Offload to RDMA NIC
IX, Arrakis, SandStorm, mTCP, LibVMA, OpenOnload…
Rsocket, SDP, FreeFlow…
User App
User-space VFS
User App
User-space VFS
Host 1
TCP/IP
TCP/IP
User App
Host 2
Kernel TCP/IP
NIC packet API
User-space TCP/IP
User-space TCP/IP
NIC packet API
NIC packet API
Kernel
NIC packet API
User-space Stack
User App
User-space VFS
User App
User-space VFS
Host 1
RDMA
User App
Host 2
NIC RDMA API Hardware-based Transport
NIC RDMA API
User-space VFS
Notes: There have been extensive research to improve the performance of socket systems.
The first category is to optimize the kernel. A socket stack basically divides into three layers. The first layer is the virtual file system, VFS, because each socket connection is regarded as a file in Linux, and a file descriptor is mapped for the socket. The second layer is the kernel TCP/IP stack that provides the transport function. The third layer is the hardware interface layer. Linux kernel uses a packet API.
The second category is to implement the VFS abstraction and TCP/IP transport in the user space. It not only move the kernel functions into user space, but also greatly simplify the functions, for example, use polling to avoid the interrupt and process scheduling overheads.
The third category is to offload the transport to the NIC. Here we recall some history of hardware-based transports. TCP offload is not a new thing. In 1990s, there has been Ethernet cards that

## Slide 5: Linux Socket: from send() to recv()
OS
NIC
Sender Host
Application
Lock
send() syscall
VFS send
Copy data, allocate mem
TCP/IP
TCP send buffer
Network packet
C library
send() socket call
OS
NIC
Receiver Host
Application
Lock
recv() syscall
VFS recv
Copy data, free mem
TCP/IP
TCP recv buffer
Network packet
C library
recv() socket call
Event Notification
Wakeup process
Process Scheduling
Network packet
Packet processing (netfilter, tc…)
Network packet
Packet processing (netfilter, tc…)
Network packet

## Slide 6: Round-Trip Time Breakdown
Type | Overhead (ns) | Linux |  | LibVMA |  | RSocket |  | SocksDirect | 
 |  | Inter-host | Intra-host | Inter-host | Intra-host | Inter-host | Intra-host | Inter-host | Intra-host
Per operation | Total | 413 |  | 177 |  | 209 |  | 53 | 
 | C library shim | 12 |  | 10 |  | 10 |  | 15 | 
 | Kernel crossing (syscall) | 205 |  | N/A |  | N/A |  | N/A | 
 | Socket FD locking | 160 |  | 121 |  | 138 |  | N/A | 
Per packet | Total | 15000 | 5800 | 2200 | 1300 | 1700 | 1000 | 850 | 150
 | Buffer management | 430 |  | 320 |  | 370 |  | 50 | 
 | TCP/IP protocol | 360 |  | 260 |  | N/A |  | N/A | 
 | Packet processing | 500 | N/A | 130 |  | N/A |  | N/A | 
 | NIC doorbell and DMA | 2100 | N/A | 900 | 450 | 900 | 450 | 600 | N/A
 | NIC processing and wire | 200 | N/A | 200 | N/A | 200 | N/A | 200 | N/A
 | Handling NIC interrupt | 4000 | N/A | N/A |  | N/A |  | N/A | 
 | Process wakeup | 5000 |  | N/A |  | N/A |  | N/A | 
Per kbyte | Total | 365 | 160 | 540 | 381 | 239 | 212 | 173 | 13
 | Copy | 160 |  | 320 |  | 160 |  | 13 | 
 | Wire transfer | 160 | N/A | 160 | N/A | 160 | N/A | 160 | N/A
Notes: Categorize into per-operation, per-packet, per-kbyte overheads.
Linux: most overheads in NIC doorbell, DMA, handling NIC interrupt and process wakeup. Other overheads also contribute a large portion of overheads.
LibVMA:

## Slide 7: SocksDirect Design Goals
Compatibility
Drop-in replacement, no application modification
Isolation
Security isolation among containers and applications
Enforce access control policies
High Performance
High throughput
Low latency
Scalable with number of CPU cores

## Slide 8: SocksDirect: Fast and Compatible Socket in User Space
Process 1
Process 2
Event queue
Request queue
Application
User Mode
Kernel Mode
Shared Buffer
Event queue
Request queue
Application
Data
Data
Monitor Process
Monitor: user-space daemon process to coordinate global resources and enforce ACL rules.
Processes as a shared-nothing distributed system: use message passing over shared-memory queues.
ACL rules
connect
send
recv
accept

## Slide 9: SocksDirect Supports Different Transports for Data
User App
libsd
User App
libsd
User App
libsd
User App
TCP/IP
TCP/IP
Monitor
Host 1
Host 2
Host 3
No SocksDirect
Monitor
Mem Queue
Mem Queue
Mem Queue
TCP/IP
RDMA
NIC RDMA API
NIC Packet API
NIC RDMA API

## Slide 10: Remove the Overheads (1)
Type | Overhead | Linux RTT (ns) |  | SocksDirect RTT (ns) | 
 |  | Inter-host | Intra-host | Inter-host | Intra-host
Per operation | Total | 413 |  | 53 | 
 | C library shim | 15 |  | 15 | 
 | Kernel crossing (syscall) | 205 |  | N/A | 
 | Socket FD locking | 160 |  | N/A | 
Per packet | Total | 15000 | 5800 | 850 | 150
 | Buffer management | 430 |  | 50 | 
 | TCP/IP protocol | 360 |  | N/A | 
 | Packet processing | 500 | N/A | N/A | 
 | NIC doorbell and DMA | 2100 | N/A | 600 | N/A
 | NIC processing and wire | 200 | N/A | 200 | N/A
 | Handling NIC interrupt | 4000 | N/A | N/A | 
 | Process wakeup | 5000 |  | N/A | 
Per kbyte | Total | 365 | 160 | 173 | 13
 | Copy | 160 |  | 13 | 
 | Wire transfer | 160 | N/A | 160 | N/A

## Slide 11: Remove the Overheads (2)
Type | Overhead | Linux RTT (ns) |  | SocksDirect RTT (ns) | 
 |  | Inter-host | Intra-host | Inter-host | Intra-host
Per operation | Total | 413 |  | 53 | 
 | C library shim | 15 |  | 15 | 
 | Kernel crossing (syscall) | 205 |  | N/A | 
 | Socket FD locking | 160 |  | N/A | 
Per packet | Total | 15000 | 5800 | 850 | 150
 | Buffer management | 430 |  | 50 | 
 | TCP/IP protocol | 360 |  | N/A | 
 | Packet processing | 500 | N/A | N/A | 
 | NIC doorbell and DMA | 2100 | N/A | 600 | N/A
 | NIC processing and wire | 200 | N/A | 200 | N/A
 | Handling NIC interrupt | 4000 | N/A | N/A | 
 | Process wakeup | 5000 |  | N/A | 
Per kbyte | Total | 365 | 160 | 173 | 13
 | Copy | 160 |  | 13 | 
 | Wire transfer | 160 | N/A | 160 | N/A

## Slide 12: Token-based Socket Sharing
Optimize for common cases.
Be correct for all cases.
Many to one
One to many
Transfer ownership of tokens via monitor.
Socket is shared among threads and forked processes.
Many to one
One to many
Sender 1
Sender 2
Receiver
Queue
Sender
Receiver 1
Receiver 2
Queue
Lock
Lock
Sender 1
Sender 2
Receiver
Queue
Sender
Receiver 1
Receiver 2
Queue
Receive
token
Send
token

## Slide 13: Handling Fork
Linux semantics requirement:
File descriptors need to be sequential (1,2,3,4,5…).
Sockets are shared for parent and child processes.
Parent process
Child process
FD Table
5 (COW)
FD Table
5 (COW)
Shared pages
FD Table
3
4
SHM (shared)
RDMA QP
3 (on demand)
5
SHM (shared)
SHM Queue
4
SHM (private)
Socket Data
5
Socket Data
3
4
RDMA QP
3
Transport limitations:
RDMA QP cannot be shared among processes.
Socket Data
3
4
5
RDMA QP
3
5

## Slide 14: Remove the Overheads (3)
Type | Overhead | Linux RTT (ns) |  | SocksDirect RTT (ns) | 
 |  | Inter-host | Intra-host | Inter-host | Intra-host
Per operation | Total | 413 |  | 53 | 
 | C library shim | 15 |  | 15 | 
 | Kernel crossing (syscall) | 205 |  | N/A | 
 | Socket FD locking | 160 |  | N/A | 
Per packet | Total | 15000 | 5800 | 850 | 150
 | Buffer management | 430 |  | 50 | 
 | TCP/IP protocol | 360 |  | N/A | 
 | Packet processing | 500 | N/A | N/A | 
 | NIC doorbell and DMA | 2100 | N/A | 600 | N/A
 | NIC processing and wire | 200 | N/A | 200 | N/A
 | Handling NIC interrupt | 4000 | N/A | N/A | 
 | Process wakeup | 5000 |  | N/A | 
Per kbyte | Total | 365 | 160 | 173 | 13
 | Copy | 160 |  | 13 | 
 | Wire transfer | 160 | N/A | 160 | N/A

## Slide 15: Per-socket Ring Buffer
Many sockets share a ring buffer
Receiver segregates packets from the NIC
Buffer allocation overhead
Internal fragmentation
tail
head
tail
head
Traditional ring buffer
SocksDirect per-socket ring buffer
One ring buffer per socket
Sender segregates packets via RDMA or SHM address
Back-to-back packet placement
Minimize buffer mgmt. overhead

## Slide 16: Per-socket Ring Buffer
tail
send_next
head
Sender side
Receiver side
RDMA write data
RDMA write credits (batched)
Two copies of ring buffers on both sender and receiver.
Use one-sided RDMA write to synchronize data from sender to receiver, and return credits (i.e. free buffer size) in batches.
Use RDMA write with immediate verb to ensure ordering and use a shared completion queue to amortize polling overhead.

## Slide 17: Remove the Overheads (4)
Type | Overhead | Linux RTT (ns) |  | SocksDirect RTT (ns) | 
 |  | Inter-host | Intra-host | Inter-host | Intra-host
Per operation | Total | 413 |  | 53 | 
 | C library shim | 15 |  | 15 | 
 | Kernel crossing (syscall) | 205 |  | N/A | 
 | Socket FD locking | 160 |  | N/A | 
Per packet | Total | 15000 | 5800 | 850 | 150
 | Buffer management | 430 |  | 50 | 
 | TCP/IP protocol | 360 |  | N/A | 
 | Packet processing | 500 | N/A | N/A | 
 | NIC doorbell and DMA | 2100 | N/A | 600 | N/A
 | NIC processing and wire | 200 | N/A | 200 | N/A
 | Handling NIC interrupt | 4000 | N/A | N/A | 
 | Process wakeup | 5000 |  | N/A | 
Per kbyte | Total | 365 | 160 | 173 | 13
 | Copy | 160 |  | 13 | 
 | Wire transfer | 160 | N/A | 160 | N/A

## Slide 18: Payload Copy Overhead
Why both sender and receiver need to copy payload?
App
send(buf, size);
memcpy(buf, data, size);
NIC
DMA
Mem
DMA read
Wrong data
Sender
Receiver
NIC
user_buf = malloc(size);
DMA to socket buf
Mem
App
Network packet
DMA read
recv(user_buf, size);
Copy socket buf to user buf
Notify event (epoll)

## Slide 19: Page Remapping
Problem: page remapping needs syscalls!
Map 1 page: 0.78 us
Copy 1 page: 0.40 us
Solution: batch page remapping for large messages
Map 32 pages: 1.2 us
Copy 32 pages: 13.0 us
Virtual addr
New page
Sender
Send physical page
Data page
Virtual addr
Old page
Receiver

## Slide 20: Remove the Overheads (5)
Type | Overhead | Linux RTT (ns) |  | SocksDirect RTT (ns) | 
 |  | Inter-host | Intra-host | Inter-host | Intra-host
Per operation | Total | 413 |  | 53 | 
 | C library shim | 15 |  | 15 | 
 | Kernel crossing (syscall) | 205 |  | N/A | 
 | Socket FD locking | 160 |  | N/A | 
Per packet | Total | 15000 | 5800 | 850 | 150
 | Buffer management | 430 |  | 50 | 
 | TCP/IP protocol | 360 |  | N/A | 
 | Packet processing | 500 | N/A | N/A | 
 | NIC doorbell and DMA | 2100 | N/A | 600 | N/A
 | NIC processing and wire | 200 | N/A | 200 | N/A
 | Handling NIC interrupt | 4000 | N/A | N/A | 
 | Process wakeup | 5000 |  | N/A | 
Per kbyte | Total | 365 | 160 | 173 | 13
 | Copy | 160 |  | 13 | 
 | Wire transfer | 160 | N/A | 160 | N/A
Notes: Go through very fast.

## Slide 21: Process Wakeup Overhead
Problem: multiple processes share a CPU core
Linux process wakeup (mutex, semaphore, read): 2.8 ~ 5.5 us
Cooperative context switch (sched_yield): 0.2 us
Solution:
Pin each thread to a core
Each thread poll for some time slice, and sched_yield after then.
All threads on the core run in round-robin order.
Notes: Go through very fast.

## Slide 22: Summary: Overheads & Techniques
Kernel crossing (syscall) Monitor and library in user space. Shared-nothing, use message passing for communication.
TCP/IP protocol Use hardware-based transports: RDMA / SHM.
Locking of socket FDs Token-based socket sharing. Optimize common cases, prepare for all cases.
Buffer management Per-socket ring buffer.
Payload copy Batch page remapping.
Process wakeup Cooperative context switch.

## Slide 23: Evaluation Setting
User App
libsd
User App
libsd
User App
libsd
Monitor
Host 1
Host 2
Monitor
Mem Queue
Mem Queue
Mem Queue
RDMA
NIC RDMA API
NIC RDMA API
Notes: Use LD_PRELOAD to load libsd library.
Intra-host
Inter-host

## Slide 24: Latency
Intra-host
Inter-host
Notes: Intra-host: 8B latency close to shared memory queue, 4x lower than Rsocket and LibVMA because they use NIC to forward intra-host packets. 35x lower than Linux.
Inter-host: 8B latency even lower than two-sided RDMA send and receive, because we use one-sided RDMA write. Half of Rsocket, performance gain due to buffer management. 7x lower than LibVMA because it needs batching. Latency 17x lower than Linux.

## Slide 25: Throughput
Intra-host
Inter-host
Notes: Intra-host: 8B message throughput 20x of Linux. At 8K it is closest to other systems because we need batching for zero copy, and it is only activated for >=16KB messages. Large messages 13x of Linux.
Inter-host: 8B message throughput 15x of Linux. One socket connection can saturate the 100Gbps link.

## Slide 26: Multi-core Scalability
Intra-host
Inter-host
Notes: Multi-core scalability: SocksDirect almost linearly scalable. Other systems not linearly scalable due to file descriptor locking and packet queue contention. With higher number of cores, the throughput is even worse.
For inter-host, SocksDirect has even higher throughput than bare metal RDMA, because we have batching.

## Slide 27: Application Performance
Nginx HTTP server request latency
Notes: Nginx HTTP server between two hosts: small HTTP messages, 5x lower than Linux. For large message, 13x lower than Linux due to zero copy.

## Slide 28: Limitations
Scale to many connections
RDMA scalability: under high concurrency, NIC cache miss will degrade throughput. Recent NICs have larger cache.
Connection setup latency: future work.
Congestion control and QoS
Emerging RDMA congestion control (e.g. DCQCN, MP-RDMA, HPCC) and loss recovery (e.g. MELO) mechanisms in hardware.
QoS: OVS offload in RDMA NICs, or use programmable NICs.
Scale to many threads
Monitor polling overhead

## Slide 29: Conclusion
Contributions of this work:
An analysis of performance overheads in Linux socket.
Design and implementation of SocksDirect, a high performance user space socket system that is compatible with Linux and preserves isolation among applications.
Techniques to support fork, token-based connection sharing, allocation-free ring buffer and zero copy that may be useful in many scenarios other than sockets.
Evaluations show that SocksDirect can achieve performance that is comparable with RDMA and SHM queue, and significantly speedup existing applications.

## Slide 30: Thank you!
Notes: Thank you for listening!

## Slide 32: High Performance Socket Systems
Kernel Optimization
FastSocket, Megapipe, StackMap…
Good compatibility, but leave many overheads on the table.
User-space TCP/IP Stack
IX, Arrakis, SandStorm, mTCP, LibVMA, OpenOnload…
Does not support fork, container live migration, ACLs…
Use NIC to forward intra-host packets (SHM is faster).
Fail to remove payload copy, locking and buffer mgmt overheads.
Offload to RDMA NIC
Rsocket, SDP, FreeFlow…
Lack support for important APIs (e.g. epoll).
Same drawbacks as user-space TCP/IP stacks.
Notes: Kernel Optimization
Good compatibility, but leave many overheads on the table.
User-space TCP/IP Stack
Does not support fork, container live migration, ACLs…
Use NIC to forward intra-host packets (SHM is faster).
Fail to remove payload copy, locking and buffer mgmt overheads.
Offload to RDMA NIC
Rsocket, SDP, FreeFlow…
Lack support for important APIs (e.g. epoll).
Same drawbacks as user-space TCP/IP stacks.

## Slide 33: The Slowest Part in Linux Socket Stack
Virtual File System
TCP/IP Protocol
Application
socket send / recv
Loopback interface
Virtual File System
Application
pipe read / write
10 us RTT
0.9 M op/s tput
8 us RTT
1.2 M op/s tput
TCP/IP protocol is NOT the slowest part!

## Slide 34: Payload Copy Overhead
Solution: page remapping
Sender
A
1
B
C
2
Receiver
B’
①
④
⑤
B’
RDMA write
③
②
⑥
B’
C
⑦

## Slide 35: Socket Queues
S1
3,4
FD
3
4
5
S2
5
Sender
Receiver
R1
3
R2
4,5
Monitor
3: S1→R1, 4: S1→R2, 5: S2→R2
Socket Queues

## Slide 36: Connection Management
Connection setup procedure

## Slide 37: Token-based Socket Sharing
Takeover: transfer token among threads.
Sender 1
Sender 2
Receiver
Data Queue
Send
token
Monitor
Takeover request
Takeover request
Send
token

## Slide 38: Rethink the Networking Stack
NIC
Software Stack
Application
Socket
RDMA
SocksDirect
eRPC
RPC
Packet
LITE
LITE
RDMA
Communication primitive
HW/SW work split